## Slide 1: PMIPv6 Extension for Multicast draft-asaeda-multimob-pmip6-extension-05
Hitoshi Asaeda
Pierrick Seite
Jinwei Xia
80th IETF, March 2011, Prague, Czech Republic

## Slide 2: Protocol Extensions
Traffic aggregation
  Set up a bi-directional tunnel link (M-Tunnel) between LMA and MAG for traffic aggregation
    M-tunnels are dedicated to multicast data and message transmission between LMA and MAG and shared by all MNs at the MAG
Seamless handover
  PBU with multicast extension (PBU-M) message
  Compliant with M-CTD with CXTP [RFC4067] or Policy Profile
No multicast protocol changes

## Slide 3: Supported Functions
Provide flexibility with various scenarios
  LMA can be a PIM-SM router / MLD proxy
  MAG can be a PIM-SM router / MLD proxy
  No changes for mobile nodes
Support local routing (when MAG acts as a PIM router)
Address tunnel convergence problem (when MAG acts as a PIM router)
Not discussed in this document
  Source mobility
    Possible, when MAG acts as a PIM router
  Dual-stack support
    Possible, if some external function is used
  Dual-mode MAG/LMA (e.g., MAG operating both PIM and MLD proxy)
    Avoid its complexity

## Slide 4: Scenario – 1
Fixed Internet
Src
LMA
MAG
Src
MN
MN
MN
M-Tunnel
MLD proxy
PIM-SM
Upstream Interface
Downstream Interface
Src
LMA
MAG
PMIPv6-Domain
MR

## Slide 5: Scenario – 2
Fixed Internet
LMA
MAG
MAG
Src
MN
MN
MN
M-Tunnel
MLD proxy
PIM-SM
Upstream Interface
Downstream Interface
PMIPv6-Domain
Src
Src
LMA

## Slide 6: Scenario – 3
Fixed Internet
LMA
MAG
MAG
Src
MN
MN
MN
M-Tunnel
MLD proxy
PIM-SM
Upstream Interface
Downstream Interface
PMIPv6-Domain
Src
Src
LMA

## Slide 7: Multicast Tunnel (M-Tunnel)
Bi-directional IPv6-in-IPv6 tunnel for MLD and PIM message transmissions between LMA and MAG
Src: LMAA
Dst: Proxy CoA
Src: LMA-LL or MAG-LL
Dst: G, AllNodes, or RptAddr
MLD
Src: LMAA
Dst: Proxy CoA
Src: LMA-LL or MAG-LL
Dst: PIM-X
PIM
LMAA: LMA global address
Proxy-CoA: MAG global address
LMA-LL: LMA link-local address
MAG-LL: MAG link-local address
MLD message
PIM message
RptAddr: MLDv2 Report address
PIM-X: All-PIM-Rtr, PIM RP, etc.

## Slide 8: Multicast Tunnel (M-Tunnel)
Bi-directional IPv6-in-IPv6 tunnel for IP multicast data transmissions between LMA and MAG
  Source mobility can be supported in our infrastructure, while the detail discussion is out of scope of this document
Src: LMAA
Dst: Proxy CoA
Src: S
Dst: G
Data
LMAA: LMA global address
Proxy-CoA: MAG global address
Multicast data
S: source address
G: multicast (group) address

## Slide 9: Basic Data Flow – Ex.1
MAG acts as an MLD proxy, and LMA acts as a PIM-SM router
MN1
MN2
MAG
LMA
MLD Report
(S1,G1)
MLD Report
M-Tunnel
MLD Report
(S1,G1)
Source
PIM join

## Slide 10: Basic Data Flow – Ex.2
Both MAG and LMA act as PIM-SM routers
  RPF IF for (S1,G1) is MAG’s M-Tunnel IF
  RPF IF for (S2,G2) is MAG’s physical IF
MN1
MN2
MAG
LMA
MLD Report
(S2,G2)
MLD Report
M-Tunnel
MLD Report
(S1,G1)
Source
PIM join
PIM join

## Slide 11: Proxy Binding Update with Multicast Extension (PBU-M)
Extension for PMIPv6 [RFC5213]
New “multicast subscription flag (C)”
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Sequence # |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|A|H|L|K|M|R|P|C| Reserved | Lifetime |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| |
. .
. Mobility options .
. .
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

## Slide 12: Mobility Options in PBU-M
Same format of MLD report and multicast address record defined in MLDv2 [RFC3810]
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Type = 143 | Reserved | Checksum |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Reserved |Nr of Mcast Address Records (M)|
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| |
. .
. Multicast Address Record [1] .
. .
| |

## Slide 13: Multicast Context Transfer Data (M-CTD)
Extension for CXTP [RFC4067]
M-CTD format
  Receiver address
    Address of a host sending the Current-State Report
  Filter mode
    INCLUDE or EXCLUDE
  (S,G) the receiver has joined
    Null source address and multiple source addresses are allowed

## Slide 14: Basic Handover Scenario – Ex.1
MAG acts as an MLD proxy, and LMA acts as a PIM-SM router
Handover with CXTP
MN
pMAG
nMAG
LMA
MLD Report
(S1,G1)
PIM join
Detach
Attach
RS
CT-Req
CXTP
M-CTD
PBU-M with
MLD Record
PBA
RA
MLD Report

## Slide 15: Basic Handover Scenario – Ex.2
Both MAG and LMA acts as a PIM-SM router
  RPF IF for (S1,G1) is pMAG’s physical IF
  RPF IF to (S1,G1) is nMAG’s M-Tunnel IF
Handover with Policy Profile (no CXTP)
MN
pMAG
nMAG
LMA
MLD Report
(S1,G1)
PIM join
Detach
Attach
RS
PBA
RA
MN attachment event
(Acquire MN-Id and Profile)
PIM join
PBU-M with
MLD Record

## Slide 16: Conclusion
Specification for the PMIPv6 extension
Simple but effective
More improvement