## Slide 1: PCEP extensions for the computation of route offers with price draft-carrozzo-pce-pcep-route-price-00
G. Carrozzo, G. Bernini, G. Landi
{g.carrozzo, g.bernini, g.landi}@nextworks.it
Nextworks

## Slide 2: Network Service & Business Plane
NSBP includes all the functions for
  service specification and offer creation
  product offers publication
  e2e offer composition
  triggering service provisioning ( std PCE cycle + LSP setup)
  manage service operation/monitoring ( OAM)
  triggering service deletion ( LSP tear-down)

## Slide 3: Service PCE & NSBP
Domain
A
Domain
Z
Child-PCE
Child-PCE
Service
PCE
Product
Catalogue
SLA offers Controller + builder
NSBP
…
…
…
PCEP
PCEP
PCEP
route offers can be in the form of sparse multi-domain EROs + cost + price
route prices computed according to
  constraints specified by PCC:
    end points
    bw
    other metrics
    load balancing
    ...
  PCE policies (ref. RFC5394)

## Slide 4: Route price vs. route cost
Route cost(s)/metric(s) := Traffic Engineering indicators used
by the network administrator (carrier) to
optimize the usage of its network
resources
  1 IGP metric[RFC5440]
  2 TE metric[RFC5440]
  3 Hop Counts[RFC5440]
  4 Aggregate bandwidth consumption[RFC5541]
  5 Load of the most loaded link[RFC5541]
  6 Cumulative IGP cost[RFC5541]
  7 Cumulative TE cost[RFC5541]
  8 P2MP IGP metric[RFC6006]
  9 P2MP TE metric[RFC6006]
  10 P2MP hop count metric[RFC6006]
  ...
Route price := EUR/$$
refers to the customer-supplier interaction at the
business level for offering, negotiating and,
eventually, instantiating a network connectivity \
service (e.g. a [G]MPLS LSP)
  depends on strategic factors
  depends on the ingress/egress interfaces/PoPs
  influenced by the amount of mobilized network resources (route)

## Slide 5: PCEP RP Object extension
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| |P| Flags |O|B|R| Pri |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Request-ID-number |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| |
// Optional TLVs //
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
1 bit in RP object (Price Request bit)
  PCC to set P-bit in case of route offer computation
  When P-bit is set, the PCE computes a set of route offers
A PCErr message with Error-Type "Capability not supported“ sent back to PCC if PCE does not support it

## Slide 6: PRICE-INFO Object
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| priceModel | currencyType |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|priceUnitTime |priceUnitData | capUnitTime | capUnitData |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| priceValue |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| capValue |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
priceModel (8 bits): Pay-as-you-go | Flat
currencyType (24 bits): ISO-4217 currency name (e.g. EUR, USD, etc.)
priceUnitTime (8 bits): time interval for a unitary price value (mins | hours|
day | week | month | year )
priceUnitData (8 bits): data volume for a unitary price value (KB|MB|GB|TB)
priceValue (32 bits): value of the price
capUnitTime (8 bits): time unit used to express the Cap Value (same as per
priceUnitTime)
capUnitData (8 bits): data volume unit used to express the Cap Value (same as
per priceUnitData)
capValue (32 bits): upper bound for this service offer (e.g. max data volume
or time length for which the given offer is valid at the
specified price)

## Slide 7: PRICE-INFO Object
<PCRep Message> ::= <Common Header>
<response-list>
<response-list>::=<response>[<response-list>]
<response>::= <RP>
[<NO-PATH>]
[<attribute-list>]
[<path-list>]
<path-list>::=<path>[<path-list>]
<path>::= <ERO><attribute-list>
<attribute-list>::= [<price-info-list>]
[<LSPA>]
[<BANDWIDTH>]
[<metric-list>]
[<IRO>]
<metric-list>::=<METRIC>[<metric-list>]
<price-info-list>::=<PRICE-INFO>[price-info-list]
For successful route offers computation
  at least 1 PRICE-INFO object per PCRep msg (if P-bit is set in RP)
  multiple PRICE-INFO objects when more than one route offer is identified by the PCE for the same service
  All the PRICE-INFO objects carried in a path refer to the same ERO computed by the PCE
In case of unsuccessful route offers computation
  NO-PATH object is included as for standard path computation procedure

## Slide 8: Next steps
Continue collecting feedbacks
  this meeting, the mailing list, etc.
  some just received via email
Refine the document
  PRICE_INFO field as TLV?
    min bits allocated with current format
    More overhead with TLVs, but a more flexible / extensible object (e.g. express more caps)
  Discuss any framework convergence with
    pce-hierarchy-fwk
    Service-awareness metrics work (delay, jitter, etc.)
    Stateful PCE
Find consensus towards progressing to WG I-D