## Slide 1: Information Model & Encoding for WSON Impairments Validation draft-martinelli-ccamp-wson-iv-info-04 draft-martinelli-ccamp-wson-iv-encode-04
Ed: Giovanni Martinelli (Cisco)
Ed: Xian Zhang (Huawei)
Authors:
Gabriele Galimberti (Cisco)
Young Lee, Fatai Zhang (Huawei),
Andrea Zanardi, Domenico Siracusa, Federico Pederzolli (Create-Net)

## Slide 2: Outline
Provide updates on the information model.
The encoding draft just presented as a consequence of info-model updates.
Iv-Info list of changes:
  Section 2.1 “Definitions”.
  Section 3 “”ITU-T List Of Optical Parameters”.
  Appendix A. “FAQ”. Added.
Iv-encode list of changes:
  Section 2.1 “Optical Parameter”.

## Slide 3: 1. iv-info Editorial Changes:
Section 2.1 “Definitions”
  Added the “DWDM Line Segment” since introduced by G.680 and useful for other considerations.
Appendix with FAQ
  Application Codes
  Multivendor
Some Clean up in remaining sections

## Slide 4: 2a. iv-info Sec 3, List of Parameters: RECAP
Draft initially considered only content of G.680 computational model.
CCAMP received a liaison (LS78) with a full list of parameters required to apply.
This draft version:
We put the two list together and providing a minimum set of parameters.

## Slide 5: 2b. iv-info Sec 3, List of Parameters
G-1 OSNR
G-2 CD
G-3 PMD
G-4 PDL
L-1 Channel Freq Range
L-2 Modulation Format and Rate
L-3 Channel Power
L-4 Ripple
L-5 Channel ASE
L-6 Channel Chromatic Disp.
L-7 Channel Local Chromatic Disp.
L-8 DGD
L-9 PMD
L-10 PDL
L-11 Reflectance
L-12 Isolation
L-13 Channel extinction
L-14 Attenuation Coefficient
L-15 Non Linear coefficient
G.680
LS78
Minimum Set of
Parameters

## Slide 6: 1. iv-encode Changes
Version 03 had only the initial G.680 set of parameters, and reuses the encoding by G.697 appendix V.
New parameters are required as per info-model.
Room as been provided using the existing encoding schema.

## Slide 7: Details: Sec. 2.1 Optical Parameter
ParamSource:
  1: means G.697.
  0: current list of LS78 parameters (value 0, TBD)
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|S|V| Reserved | ParamSource | ParamID |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Value |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Variance (Optional) |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

## Slide 8: Details: Sec. 2.1 Optical Parameter
ParamSource = 0
ParamID.
. . .
1. Ripple (dBm). L-4 in ...
2. Channel signal-spontaneous noise figure. L-5 ...
3. DGD, Differential Group Delay. L-8 in ...
4. Reflectance. L-11 in ...
5. Isolation. L-12 in ...
6. Channel extintion. L-13 in ...
7. Attenuation Coefficient. L-14 in ...

## Slide 9: Conclusion
With latest updates both drafts are in good shape.
Authors think drafts are ready for WG adoption.
  Natural evolution of existing wson document
  Will continue to evolve according to WG inputs and future ITU Liaisons.
THANK YOU!