## Slide 1: MPLS Architectural Principles
George Swallow
(swallow@cisco.com)
Notes: 1

## Slide 2: MPLS Guiding Principles
Co-existence with IP
IP based Control Planes
Reuse of IP protocols
Extendable protocols
Pragmatism

## Slide 3: MPLS Architectural Principles
Separation of Control Plane and Data Plane
Label semantics (except reserved) belong to application
  Forwarding Equivalence Class
Compact Header
Multiple, Independent Control Planes
Label Stack

## Slide 4: Some contextual background
Ratio of processor speeds to data-link speed much lower
Cost of a bit orders of magnitude higher
Getting links was very slow
IP community did not like ATM and particularly the “cell tax”

## Slide 5: Dataplane Requirements
Very fast (i.e few gates and/or few cycles per packet)
Very wide range of equipment
Simple Data Plane
Stable Data Plane
  Needs to work for lifetime of equipment (>10 yrs)
    Including boxes for which
    New linecards cannot be cost justified
    Software has become “functionally stable”

## Slide 6: MPLS Components
Control components
    Applications directly define and manipulate label bindings
    Essentially they use labels to program data plane
Forwarding component
  Simple label-swapping paradigm
RSVP-TE
Pseudo-
wires
mLDP
LDP
L2VPN
L3VPN
MPLS-TP
BGP RFC3107
SDN
Efficient label processing
EVPN

## Slide 7: Simple Forwarding Plane
Label Stack Entry
Label determines simple forwarding operations
  Push, Pop, Swap, Outgoing interface(s)
Class of Service + Label defines queuing, drop priority
COS = Class of Service S = Stack Bit TTL = Time to Live
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Label | COS |S| TTL |

## Slide 8: Label Semantics
Defined by the application
Need only be known by LSRs that Push/Swap/Pop that label
Full semantics need only be known to the consumer of the label
Forwarding Equivalence Class
  Simple powerful concept
  Single label assigned to a set of packets that are to be treated identically
    Note that CoS bits are not part of this definition

## Slide 9: Label Space
One Million Labels
16 Reserved Labels
  Intentionally a limited number
  New values impact dataplane
Label Spaces per
  LSR
  Interface

## Slide 10: Context Labels
One label can define a new label space
Powerful means of expanding the available labels
If you need more labels, this is the proper way to do it!

## Slide 11: Label Stack
Arbitrary number of labels
Multiple control planes act on packets
Control planes are totally independent
Control plane at one level can be replaced
  No impact on levels above or below
Virtual Private Network
VPN
The single most important element in MPLS’ success
VPN
Virtual Private Network
Unicast Routing
Traffic Engineering
Traffic
Engineering
Unicast
Routing

## Slide 12: “No idea is so bad that it won’t be proposed over and over again”

## Slide 13: Ideas proposed over and over
Global Labels
Source Labels
Special encodings of labels
  Special meanings to label bits
Special semantics for double labels
  PoP top label; process next label; push PoP’ed label back on
  8 byte label stack entry
  Special uses for CoS and / or TTL bits
Multiple EOS bits set in the label stack

## Slide 14: Other rejected / abandoned ideas
Encoding labels into VLAN-IDs
Encoding labels into the IPv6 flow label
Label Stack Header
Labels in PIM
I’m sure I’ve missed some