## Slide 1: YANG Model for Unified+NVO3 OAM
Tissa Senevirathne
draft-tissa-nvo3-yang-oam

## Slide 2: Goal
Create a YANG model that provides a set of unified interfaces across various OAM technologies.
Facilitate “nested OAM” across layers that deploys different OAM technologies.

## Slide 3: Architecture
Top Level YANG Model provides the overall framework and setup the structures
Separate YANG model for each technology area that augments the top level model to include technology specific aspects
Application
draft-tissa-netmod-oam-01 – presents the top level YANG model
draft-tissa-trill-yang-oam-00 and draft-tissa-nvo3-yang-oam provide extensions for TRILL and NVO3

## Slide 4: YANG Model
Gen YANG
TRILL
NVO3
IP
foo
Sub-tech(vxlan)
Sub-tech (bar)
Unified API
Sub-tech (blah)

## Slide 5: Flow of the Model
MD - Level
MA
MA
MA
MD - Level
MEP
MD, MA, MEP
MD, MA, MEP
List indexed by layer offset provides MEPs of the next LAYERS below

## Slide 6: More details
module: ietf-oam
+--rw domains
| +--rw domain* [md-name]
| +--rw technology identityref
| +--rw md-name-format MD-name-format
| +--rw md-name binary
| +--rw md-level int32
| +--rw MAs!
| +--rw MA* [ma-name]
| +--rw ma-name-format MA-name-format
| +--rw ma-name binary
.
.
+--rw MEP* [mep-id]
| +--rw mep-id MEP-id
| +--rw mep-name? string
| +--rw mep-direction MEP-direction
| +--rw (mep-address)?
| | +--:(mac-address)
| | | +--rw mac-address? yang:mac-address
| | +--:(ipv4-address)
| | | +--rw ipv4-address? inet:ipv4-address
| | +--:(ipv6-address)
| | +--rw ipv6-address? inet:ipv6-address
| +--rw (context-id)?
| | +--:(context-null)
+--:(context-id-nvo3)
+--rw vni? vni

## Slide 7: Application to NVO3
We augment the nodes with NVO3 specifics
  Flow-entropy , MEP addressing, context-id

## Slide 8: Application to NVO3 continued
augment "/goam:domains/goam:domain/goam:MAs/goam:MA/goam:flow-
entropy" {
case flow-entropy-vxlan {
leaf flags-vxlan {
when "/goam:domains/goam:domain/goam:technology-sub-type=‘vxlan'";
type flags-vxlan;
}
leaf flow-entropy-vxlan {
when "/goam:domains/goam:domain/goam:technology-sub-type=‘vxlan'";
type flow-entropy-vxlan;
}
}
}
identity nvo3 {
base goam:technology-types;
description “nvo3 type";
}
augment "/goam:domains/goam:domain/goam:MAs/goam:MA/goam:context-id"
{
case context-id-nvo3 {
leaf vni {
when "/goam:domains/goam:domain/goam:technology-type=‘nvo3'";
type vni;
}
}
}
Augment based on technology
augment "/goam:domains/goam:domain/goam:MAs/goam:MA" {
leaf technology-sub-type {
when "/goam:domains/goam:domain/goam:technology=‘nvo3'";
type identityref {
base technology-sub-type;
}
}
}

## Slide 9: MEP Addressing for NVO3
NVE can have multiple IP addresses, shared between multiple VNI
Within NVE multiple VNI
MEP address is a list [Dst IP , VNI]
Overlay MEP: VNI
Underlay MEP:IP
Proposal - 1
Proposal - 2
Preferred
(ref:draft-ietf-nvo3-arch)

## Slide 10: References
High level YANG model
  https://datatracker.ietf.org/doc/draft-tissa-netmod-oam/
Technology dependent
  TRILL: http://tools.ietf.org/html/draft-tissa-trill-yang-oam-00
  NVO3:http://tools.ietf.org/html/draft-tissa-nvo3-yang-oam-00

## Slide 11: Q&A
Reviews and feedback - is the YANG model extensible ?
  Based on feedback received so far some of the technology specific nodes e.g. CCM removed from gen-oam
Next steps
  Request WG to expand charter to include related YANG models and management and OAM in general.
  Adopt OAM YANG model as part of the WG