## Slide 1
Service Function Chaining
Use Case for SPRING
draft-xu-spring-sfc-use-case-02
Xiaohu Xu (Huawei)
Zhenbin Li (Huawei)
Himanshu Shah (Ciena)
Luis M. Contreras (Telefonica I+D)
IETF90, Toronto

## Slide 2
Service Function (SF): A function that is responsible for specific treatment of received packets.
SF ID: A unique identifier that represents a service function within an SFC-enabled domain.
Service Node (SN): A physical or virtual element that hosts one or more service functions and has one or more network locators associated with it for service delivery.
Service Function Chain (SFC): An ordered set of service functions that must be applied to packets and/or frames selected as a result of classification
Service Function Path (SFP): The instantiation of an SFC in the network.
Network Forwarder (NF): SFC network forwarders provide network connectivity for SFF and SF.
Service Function Forwarder (SFF): is responsible for delivering traffic received from the SFC network forwarder to one or more connected service functions via information carried in the SFC encapsulation.
SFC Background
Service Node (SN)
SFC-unaware SF
SF
SFF
SFC Proxy
SFC-aware SF
NF
Service Node
(SN)
Service Node
(SN)
Service Classifier
(SC)

## Slide 3
When applying a particular SFC (e.g., {SF1,SF3}) to the selected traffic, the traffic needs to be steered through the corresponding SFP (e.g.,{SN1, SF1, SN2, SF3}) in the SFC-enabled network.
It’s obvious that the SPRING-based source routing mechanism could be leveraged to steer the traffic through a particular SFP.
  The SFP (or the SFC) information could be encoded in the MPLS label stack or the IPv6-SR header. To simplify the illustration, only MPLS-SPRING-based SFC is discussed here.
Motivation
SN1
SN2
SC
Z
Packet to Z
Packet to Z
SID (SN2)
SID (SF3)
SID (SN1)
SID (SF1)
SF1
SF2
SF3
Packet to Z
SID (SN2)
SID (SF3)
Packet to Z
The packet is selected to travel through an SFC {SF1, SF3}.
SR/SFC Domain

## Slide 4
Service Nodes (SN) allocate local MPLS labels for their associated SFs.
An MPLS label stack indicating a particular SFP (i.e., an ordered list of SNs and SFs) to be traversed is imposed on the selected packet by the Classifier.
Encoding the SFP as an Label Stack
SN1
SN2
SC
Z
Packet to Z
Packet to Z
1002
103
1001
101
SF1
SF2
SF3
Packet to Z
1002
103
Packet to Z
The packet is selected to travel through an SFC {SF1, SF3}.
SR/SFC Domain
SID:101
SID:102
SID:1001
SID:1002
SID:103

## Slide 5
Service Nodes (SN) allocate local MPLS labels for their associated SFs.
An MPLS label stack indicating a particular SFP (i.e., an ordered list of SNs and SFs) to be traversed is imposed on the selected packet by the Classifier.
When SNs are separated by IP networks, IP tunnels (e.g., MPLS-over-GRE) instead of LSPs could be used between SNs.
Encoding the SFP as an Label Stack (cont)
SN1
SN2
SC
Z
Packet to Z
Packet to Z
1002
103
1001
101
SF1
SF2
SF3
Packet to Z
1002
103
Packet to Z
The packet is selected to travel through an SFC {SF1, SF3}.
SR/SFC Domain
SID:101
SID:102
SID:1001
SID:1002
SID:103
IP (SC->SN1)
IP (SN1->SN2)
This label would be striped if it’s a PHP label.
This label would be striped if it’s a PHP label.

## Slide 6
Once global labels are allocated for SFs, the Classifier could choose to impose an MPLS label stack just indicating a particular SFC (i.e., an ordered list of SFs),
  SNs/Classifiers should be capable of resolving the appropriate SN for the next SF.
Encoding the SFC as a Label Stack
SN1
SN2
SC
Z
Packet to Z
Packet to Z
103
1001
101
SF1
SF2
SF3
Packet to Z
1002
103
Packet to Z
The packet is selected to travel through an SFC {SF1, SF3}.
SR/SFC Domain
SID:101
SID:102
SID:1001
SID:1002
SID:103
103->103|1002
->103|1004
101->101|1001
->101|1003
SN4
SF3
SID:103
SN3
SF1
SID:101
SID:1003
SID:1004
SFLB:{100, 199}

## Slide 7
Once global labels are allocated for SFs, the Classifier could choose to impose an MPLS label stack just indicating a particular SFC (i.e., an ordered list of SFs),
  SNs/Classifiers should be capable of resolving the appropriate SN for the next SF.
  When SNs are separated by IP networks, IP tunnels (e.g., MPLS-over-GRE) instead of LSPs could be used between SNs. Furthermore, no need for node SIDs anymore.
Encoding the SFC as a Label Stack
SN1
SN2
SC
Z
Packet to Z
Packet to Z
103
IP(SC->SN1)
101
SF1
SF2
SF3
Packet to Z
IP(SN1->SN2)
103
Packet to Z
The packet is selected to travel through an SFC {SF1, SF3}.
SR/SFC Domain
SID:101
SID:102
SID:103
103->103|IP(SN2)
->103|IP(SN4)
101->101|IP(SN1)
->101|IP(SN3)
SN4
SF3
SID:103
SN3
SF1
SID:101
SFLB:{100, 199}

## Slide 8
A common label block, referred to as SF Label Block (SFLB) is reserved by all SNs and Classifiers for SF SIDs.
The unique label for a given SF could be automatically determined by adding the SF ID of that SF to the first label value of the above SFLB.
How to Allocate Global Labels for SFs
SN1
SN2
SC
Z
SF1
SF2
SF3
SR/SFC Domain
SID:101
SID:102
SID:1001
SID:1002
SID:103
SN4
SF3
SID:103
SN3
SF1
SID:101
SID:1003
SID:1004
SFLB:{100, 199}

## Slide 9
WG adoption?
Next Step