## Slide 1: The Benefits to Applications of using Explicit Congestion Notification (ECN) draft‐welzl‐ecn‐benefits
Michael Welzl (University of Oslo)
Gorry Fairhurst (University of Aberdeen)
90th IETF Meeting
Toronoto, July 2014

## Slide 2: Draft goals
Goals:
– document gains of ECN
– includes less obvious gains
– may include deployment scenarios to illustrate benefit
Non-goals:
– it does not recommend any router/endpoint behaviour
- it does not define new mechanisms
. . . in short, "a Manifesto for deploying ECN"

## Slide 3: ECN advantages seem obvious
• ECN marks instead of dropping ECN-capable packets
A receiver gets packets instead of loosing them [RFC2884]
However, often few congestion drops [RFC3649]
• Biggest gain can be congestion indication without loss recovery
Reduced Head-­of­‐Line Blocking for in-order transports
Reduced probability of timeout (RTO Expiry)
- RTO collapses cwnd, with significant bad impact
Some applications do not retransmit lost packets
Typically VoIP, interactive video, realtime data
- Needs loss­hiding mechanisms, impacts perceived quality

## Slide 4: Main Message
People should configure host stacks and network devices to enable ECN - because it will make things better!
Application developers should, where possible, use transports that enable ECN - because this will make things better, without people needing to rewrite apps!
We think this document is useful!
- Is anyone able to help us articulate the gains?
- Can we make this a WG item (in tsvwg or the AQM wg)?