## Slide 1: Application-aware Targeted LDP draft-esale-mpls-app-aware-tldp-01
draft-esale-mpls-app-aware-tldp-01
IETF-91 (Honolulu)
speaker: Santosh Esale
Santosh Esale (sesale@juniper.net) Raveendra Torvi (rtorvi@juniper.net)
Chris Bowers (cbowers@juniper.net)
Luay Jalil (luay.jalil@verizon.com)
Uma Chunduri (uma.chunduri@ericsson.com)
Zhenbin Li (lizhenbin@huawei.com)

## Slide 2
What is this draft about
draft-esale-mpls-app-aware-tldp-01
Initiating and responding LSR are made aware
of targeted LDP application that needs a tLDP session
Benefits:
Establishment of automatic tLDP session based on
negotiated targeted LDP applications
Establishment of limited number of tLDP sessions for certain automatic applications
Targeted application is mapped to LDP FEC elements to advertise only necessary FEC label bindings over the session

## Slide 3
Protocol changes
Advertise and negotiate targeted applications capability (TAC) during tLDP session initialization
The TAC TLVs capability data consists of one or more targeted application element (TAE) each pertaining to unique targeted application
On the receipt of a valid TAC TLV, an LSR must generate its own TAC TLV with TAEs
If there is at least one TAE common between the TAC TLV it has received and its own, the tLDP session proceed to establishment as per RFC 5036. If not, a LSR sends a ‘Session Rejected/Targeted Application Capability Mis-Match’ message to the peer and close the session
Se
draft-esale-mpls-app-aware-tldp-01

## Slide 4
New in version 01
draft-esale-mpls-app-aware-tldp-01
Additional co-authors
New use case – mLDP node protection
Added examples of application capability negotiations
Terminology changed : Sender/Receiver LSR  Initiating/Responding LSR

## Slide 5
Use cases
1. Remote LFA
2. FEC 129
3. LDP over RSVP tunneling
4. mLDP node protection
draft-esale-mpls-app-aware-tldp-01

## Slide 6
Next steps
draft-esale-mpls-app-aware-tldp-01
Summary
01 version addresses all the received comments
Draft addresses real deployment use-cases
The authors would like to request a working group adoption