## Slide 1: Path Computation Element (PCE) Discovery using Domain Name System(DNS) draft-wu-pce-dns-pce-discovery-07
Qin Wu (sunseawq@huawei.com )
Dhruv Dhody (dhruv.dhody@huawei.com )
Daniel King (daniel@olddog.co.uk )
Diego R. Lopez (diego@tid.es )
Jeff Tantsura (Jeff.Tantsura@ericsson.com )
IETF 91
Honolulu, Canada

## Slide 2: Status of this I-D
First presented in IETF 87, Berlin meeting, agreed to address differences between the PCE and DNS domains
Follow-up in IETF 88 Vancouver meeting
  Allow NAPTR query for a specific PCE domain by linking PCE domain with DNS domain name (i.e., PCE domain added as subdomain of DNS domain name)
  Define format of TXT record value field using syntax defined in RFC1464
  Allow feature Negotiation capability by extending NAPTR service field format
  Support Discovery of PCE server with TLS support by extending NAPTR transport field format
Follow-up in IETF 89 London meeting
  Use “pce+acronym” instead of “pce+apX” in the NAPTR service field format
  Remove text record format for path computation scope
Follow-up in IETF90 Toronto meeting
  Add a DCI use case to clarify IGP inefficiency to handle a large number of PCE instances discovery.
  DNS based discovery provide better means
    Secure inter-domain discovery
      E.g., discover PCE with TLS support across domain
    Handling PCE Identity change
    Provide better load balance in case of multiple PCE instances
The latest update before IETF91, compared to v(-06):
  Add implementation update.

## Slide 3: The prototype using the DNS-based discovery proposal
The cloud infrastructure use virtual machines with custom images to run vPCE.
The cloud infrastructure assigned each vPCE a new IP address from a pool of available IP addresses.
The PCE DNS server is notified with the new IP address for a new available vPCE.
A PCC may use DNS to discover a PCE only when it needs to compute a path.
Case1: intermittent PCEP session
  systematically opened and closed for each PCEP request in the virtualized environment
Case 2: load balancing among multiple vPCEs
  Multiple vPCEs (with different IP addresses) are identified via DNS using a single PCE server name
  in the event of failure of the VNFs, a new VNF or VM (hosting the VNFs) may be spawned
    without having to update PCE reachability information on the PCC
    or flooding the IGP with the PCE location each time the IP address changes.

## Slide 4: Details of prototyping
Full details of the prototyping can be found at:
R. Vilalta, R. Munoz, R. Casellas, R. Martinez, V. Lopez, D. Lopez "Transport PCE Network Function Virtualization", in Proc. of European Conference on Optical Communication (ECOC 2014), September 21-25, Cannes (France).
<http://www.vlopezalvarez.com/Profesional/Publications/ Conferences/2014_ECOC_2.pdf>

## Slide 5: Next Steps
Well discussed on PCE list
  Integrated cross WG input
Good progress on Implementation development
(Re)requesting WG adoption
Questions?