## Slide 1: Recursive Internet Architecture EC-Funded projects IRATI, GN3+ OC.IRINA and PRISTINE
Dimitri Staessens – Ghent Uni. iMinds (BE)

## Slide 2: Current challenges
explosion in the complexity of the overall system (hundreds of protocols and thousands of standards documents)
security
scalability issues with the routing system
  (IPv6/BGP multihoming)
  Mobile end-users
Application mobility

## Slide 3: Production environment
ever growing customer base
ever growing number of devices
new and more demanding services
“worse is better”
RAD of services
fast deployment

## Slide 4: RINA
A brief introduction to the Recursive Internet Architecture

## Slide 5: Extending the IPC model

## Slide 6: Providing IPC services (with different characteristics) over different scopes
IP (L3)
Ethernet (L2)
Physical Media (L1)
Applications
TCP/UDP (L4)
IEEE 802.1Q (L2)
IEEE 802.1ah (L2)
10GBASE-ER (L1)
Applications
MPLS (L2.5)
IP (L3)
IP (L3)
UDP (L4)
VXLAN(L2)
IP (L3)
UDP (L4)
Physical Media
Applications
IPC
IPC
IPC
IPC
IEEE 802.3 (L2)
Theory
Everyday practice
RINA

## Slide 7: IPC API
APs communicate using a port, identified by a portId
6 operations:
  int _registerApp(appName, List<difName>)
  portId _allocateFlow(destAppName, List<QoSParams>)
  int _write(portId, sdu)
  sdu _read(portId)
  int _deallocate(portId)
  int _unregisterApp(appName, List<difName>)
QoSParams are defined in a technology-agnostic way
  Bandwidth-related, delay, jitter, in-order-delivery, loss rates, …

## Slide 8: Distributed Applications Provide IPC services
host
host
Edge router
Edge router
Internal AS router
X
Y
A1
A2
B1
B2
C2
C1
E1
E2
F1
F2
F3
F4
D1
D3
D2

## Slide 9: Architectural Model
DIF
System (Host)
IPC Process
Shim IPC Process
Mgmt
Agent
System
(Router)
Shim IPC Process
Shim IPC Process
IPC Process
Mgmt
Agent
System
(Host)
IPC Process
Shim IPC Process
Mgmt
Agent
Appl.
Process
Shim DIF
over TCP/UDP
Shim DIF
over Ethernet
Appl.
Process
IPC API
Data Transfer
Data Transfer Control
Layer Management
SDU Delimiting
Data Transfer
Relaying and Multiplexing
SDU Protection
Transmission Control
Retransmission Control
Flow Control
RIB Daemon
RIB
CDAP Parser/Generator
CACEP
Enrollment
Flow Allocation
Resource Allocation
Forwarding Table Generator
Authentication
State Vector
State Vector
State Vector
Data Transfer
Data Transfer
Transmission Control
Transmission Control
Retransmission Control
Retransmission Control
Flow Control
Flow Control
IPC Resource Mgt.
DIF Allocator
SDU Protection
Multiplexing
IPC Mgt. Tasks
Other Mgt. Tasks
Application Specific Tasks
Increasing timescale (functions performed less often) and complexity

## Slide 10: FP7 IRATI – overview

## Slide 11: IRATI - Introduction
FP7 Project – Jan 2013 to Dec 2014 (2 years)
5 partners
  [Research] Fundació Privada i2CAT (Spain)
  [Research] iMinds VZW(Belgium)
  [SME] Nextworks s.r.l. (Italy)
  [Industry] Interoute (UK/Italy)
  [Academia] Boston University (US)

## Slide 12: IRATI
Validation of RINA concepts
FOSS implementation of core functionalities
  IPC Process / IPC Manager daemons
  Transport and management tasks
Stack publicly available on GitHub ~ 11/2014

## Slide 13: IRATI OS/Linux implementation
Source: S. Vrijders, F. Salvestrini, E.Grasa, M. Tarzan, L. Bergesio, D. Staessens, D. Colle “ Prototyping [RINA], the IRATI project approach”, IEEE Network, March 2014

## Slide 14: IRATI Prototype initial tests
Source: S. Vrijders et al. “Experimental evaluation of RINA Prototype”, IEEE Globecom, Dec 2014

## Slide 15: Link-state routing test (IS-IS based)

## Slide 16: GEANT3+ IRINA – overview

## Slide 17: IRINA - Intro
Investigating RINA as the next generation GEANT and NREN network architecture (IRINA)
GEANT3+ project
  Starts Oct 2013, ends March 2015 (18 months)
4 Partners:
  [Research] iMinds VZW(Belgium)
  [Research] Fundació Privada i2CAT (Spain)
  [Research] Waterford Institute of Technology – Telecommunications Software & Systems Group (Ireland)
  [SME] Nextworks s.r.l. (Italy)

## Slide 18: IRINA – Overview/Objectives

## Slide 19: FP7 PRISTINE – overview
Programmability in RINA

## Slide 20: PRISTINE - Intro
FP7 Project
  Starts Jan 2014, ends Jun 2016 (30 months)
  15 Partners (Research, SMEs and Industry)

## Slide 21: PRISTINE - Objectives
IRATI provides basic core packet transport functions
PRISTINE designs some advanced functions:
  security of content and application processes,
  congestion control
  protection and resilience,
  efficient topological routing
  multi-layer management
Three use-cases
  Datacenter
  Distributed cloud
  Carrier network

## Slide 22: PRISTINE Focus
DIF
IPC Process
Shim IPC Process
IPC Process
Mgmt
Agemt
IPC Process
Mgmt
Agemt
Shim DIF
over TCP/UDP
Shim DIF
over Ethernet
Appl.
Process
IPC API
Data Transfer
Data Transfer Control
Layer Management
SDU Delimiting
Data Transfer
Relaying and Multiplexing
SDU Protection
Transmission Control
Retransmission Control
Flow Control
RIB Daemon
RIB
CDAP Parser/Generator
CACEP
Enrollment
Flow Allocation
Resource Allocation
Forwarding Table Generator
Authentication
State Vector
State Vector
State Vector
Data Transfer
Data Transfer
Transmission Control
Transmission Control
Retransmission Control
Retransmission Control
Flow Control
Flow Control
Increasing timescale (functions performed less often) and complexity
Shim IPC Process
Shim IPC Process
Shim IPC Process
Appl.
Process
System (Host)
System
(Router)
System
(Host)
VNF
Mgmt
Agemt
SDK: Policies and policy sets
Cong. Ctrl.
LL
HL