## Slide 1: IGP bandwidth based metric (draft-spallagatti-rtgwg-bandwidth-based-metric-00.txt)
Santosh Pallagatti
Pushpasis Sarkar
Hannes Gredler

## Slide 2: Problem Statement
10
10
10
10
10
10
10
10
10
10
10
10
10
10
10
10
10
10
D1
D2
R2
R3
R1
L3
L2
L1
L6
L5
L4
A path with lower cost is always preferred to reach destination.
R1 can reach D1 via ECMP next-hops L1, L2 and L3.
If Link L1 and/or L2 goes down L3 will still be best path to reach D1 from R1.
R1 will use single next-hop (L3 - lower bandwidth path)to reach R1 when it could use less congested higher cost ECMP path L4, L5 and L6.
Bandwidth critical applications needs bandwidth to be satisfied.

## Slide 3: Desired behavior
10
10
10
10
10
10
10
10
10
10
10
10
10
10
10
10
10
10
D1
D2
R2
R3
R1
L3
L2
L1
L6
L5
L4
Link L1 goes down and it is ok to use L2 and L3 keep metric 10.
Assume that link L1 to L6 are 100G each.
Link L2 also goes down, path L4, L5 and L6 could be used as that is less congested. Increase metric of link L3 to 50.
50
10

## Slide 4: BBM - Interface Group
D1
D2
R2
R3
R1
L3
L2
L1
L6
L5
L4
IG1
IG2
Group | Group Bandwidth | Metric
IG1 | 200 G | 10
 | 100G | 50
 | Default | 1000
IG2 | 200G | 10
 | 100G | 50
 | Default | 1000

## Slide 5: BBM – Metric derivation
Initialize interface metric to 0 and get the cumulative group bandwidth for interface group.
Start
For all interface in group
Is group bandwidth > = Bandwidth configured?
Assign configured metric for that bandwidth to interface metric.
Is interface metric = 0
Assign default group metric to interface metric.
Stop
No
Yes
Yes
No
Active links | Total BW | BBM-metric | Remarks
L1, L2, L3 | 300G | 10 | Total BW >= 200
L1, L2 L3(down) | 200g | 10 | Total BW >= 200
L1 L2, L3(down) | 100g | 50 | 200 > Total BW >= 100

## Slide 6
Thank you