|  | INTERNATIONAL TELECOMMUNICATION UNION | COM 15 – LS 7 – E |
| --- | --- | --- |
|  | TELECOMMUNICATION STANDARDIZATION SECTOR STUDY PERIOD 2005-2008 |  |
|  |  | English only Original: English |
| Question(s): | 9, 11, 12/15 | Ottawa, 19-23 June 2006 |
| LIAISON STATEMENT |
| Source: | Q9/15, Q11/15 and Q12/15 |
| Title: | Response to your liaison statement on T-MPLS |
| To: | IETF mpls WG |
| Copy: | IETF pwe3 WG, MFA Forum |
| Approval: | By correspondence |
| For: | Comment |
| Deadline: | 16 August 2006 |
| Contact: | Malcolm Betts Nortel Networks Canada | Tel: +1 613 763 7860 Fax: +1 613 763 4371 Email: betts01@nortel.com |
|  | Ghani Abbas Marconi UK | Tel:+44 115 906 4036 Fax:+44 115 906 4346 E-mail: ghani.abbas@marconi.com |
|  | Mark Jones Sprint Corporation USA | Tel: +1 913 794 2139 Fax: +1 913 794 0415 E-mail: mark.jones@sprint.com |

Thank you for your response to our previous liaison statement.  We have the following responses to the issues that you identified.  We have attached a revised copy of G.8110.1 that we hope addresses the concerns that you have expressed.  If you have any outstanding concerns with this revised document we would appreciate a reply by the deadline indicated above.  We have another experts meeting scheduled for September 18-22, in Sophia Antipolis, France, please advise the Rapporteur if any non-ITU members wish to attend this meeting.  We will address any comments at this meeting and if necessary make adjustments to the text that we expect to approve at the SG 15 plenary meeting in October 2006.

We will keep you advised of future developments in this area and request your continuing collaboration on this work.

1. The requirements

We have not seen any documentation of the problem that T-MPLS solves.

The T-MPLS requirements are implicit based on the transport network application space.  To facilitate our communication with you we will document these implicit assumptions and requirements and send them to you as soon as they are available.

2. The reserved labels

As this is a compatibility issue, we are very concerned. We request that you document any requirements for reserved labels and bring those requirements to the MPLS Working Group in the IETF. There is a (G)MPLS change process that can be used for this "draft-andersson-rtg-gmpls-change-02.txt"

In consideration of your concerns we have agreed not to reserve any labels.  If we identify any requirements to use a reserved label in the future we will make a request to the IETF mpls Working Group as you have suggested.

We intend to update the existing T-MPLS Recommendations (G.8112 and G.8121) to reflect this decision.

3. MPLS functionality equipment T-MPLS networks.

Since we still incompatibilities between the MPLS and T-MPLS specifications we are concerned that existing MPLS equipment, even though T-MPLS is said to to be a true subset of MPLS, won't be possible to use in T-MPLS networks.

The recently introduced design with Ethernet EVCs will help to get around some of the issues we pointed out. Equipment in the T-MPLS network will not have to negotiate labels with equipment in MPLS enabled IP networks. However, we are still concerned about what "future consideration for IP/MPLS clients" might entail.

We discussed the PHP issue and understand that there is trade off between making Y.1711 OAM work and the implementation issues on not using PHP and we have understood that not using PHP is not an issue for the application scenario in the scope version 1. The need for supporting PHP in T-MPLS networks might be revisited in future versions.

In the interest of making this issue clear, we have already modified in section 6.1/G.8110.1 the sentence “The use of PHP is not supported” into “Transport MPLS LSPs do not use PHP.”

T-MPLS is intended to be a separate layer network with respect to MPLS. However, T-MPLS will use the same data-link protocol ID (e.g. EtherType), frame format and forwarding semantics for as those defined for MPLS frames.  T-MPLS and MPLS cannot coexist on the same “interface” (for example they could not coexist on a single Ethernet VLAN, however they could be multiplexed on to a common Ethernet PHY using separate VLANs).

The direct adaptation of IP/MPLS client over T-MPLS server is still at a very preliminary stage.  We would like to develop this in cooperation with the IETF.

We have also initiated work on a control plane for T-MPLS this activity is at a very preliminary stage.  If our work on T-MPLS control plane identifies requirements to modify the IETF signaling protocols or use new code points, we will submit these requirements for your consideration in accordance with the (G)MPLS change process.

In the absence of a complete description of the intended network applications we have developed the following preliminary network application examples that may be considered as we develop future versions.

Attachment: g-8110-1_ar-v2.doc

____________