| INTERNATIONAL TELECOMMUNICATION UNION | STUDY GROUP 11 |
| --- | --- |
| TELECOMMUNICATION STANDARDIZATION SECTOR STUDY PERIOD 2009-2012 | TD 396 (GEN/11) |
|  | English only Original: English |
| Question(s): | 5/11 | Geneva, 28 January 2010 |
| TEMPORARY DOCUMENT |
| Source: | Editor |
| Title: | Draft Q.3324.1: Protocol at the interface between a Transport Resource Control Physical Entity (TRC-PE) and a Transport Physical Entity (T-PE) (Rc interface): COPS alternative |

The attached draft Recommendation is output result of the January, 2010 meeting.

Draft ITU-T Recommendation Q.3324.1

Resource Control Protocol no. 4 (rcp4)
Protocol at the interface between a Transport Resource Control Physical Entity (TRC-PE) and a Transport Physical Entity (T-PE) (Rc interface): 
COPS alternative

Summary

This Recommendation provides the Stage 3 technical specifications for a protocol variant which uses COPS to satisfy the requirements for information transfer across the Rc reference point, as defined in clause 8.3 of [ITU-T Y.2111]. This protocol allows a Transport Resource Control Physical Entity (TRC-PE) to collect network topology and resource status information from elements of an access or a core network.

The COPS protocol defined in [IETF RFC 2748].

# 1	Scope

This Recommendation provides the Stage 3 technical specifications for a protocol satisfying the requirements for information transfer across the Rc reference point, as defined in clause 8.3 of [ITU-T Y.2111]. This protocol allows a Transport Resource Control Physical Entity (TRC-PE) to collect network topology and resource status information from elements of an access or a core network.

# 2	References

The following ITU-T Recommendations and other references contain provisions which, through reference in this text, constitute provisions of this Recommendation. At the time of publication, the editions indicated were valid. All Recommendations and other references are subject to revision; users of this Recommendation are therefore encouraged to investigate the possibility of applying the most recent edition of the Recommendations and other references listed below. A list of the currently valid ITU-T Recommendations is regularly published. The reference to a document within this Recommendation does not give it, as a stand-alone document, the status of a Recommendation

[ITU-T Y.2012]	ITU-T Recommendation Y.2012 (2006), Functional requirements and architecture of Release 1 of the NGN.

[ITU-T Y.2111]	ITU-T Recommendation Y.2111 (2006), Resource and admission control functions in Next Generation Networks.

[ITU-T Q.3300]	ITU-T Recommendation Q.3300 (2007), Architectural framework for the Q.33xx series of Recommendations.

[IETF RFC 2578]	IETF RFC 2578 (1999) , Structure of Management Information Version 2 (SMIv2).

[IETF RFC 2748]	IETF RFC 2748 (2000), The COPS (Common Open Policy Service) Protocol.

[IETF RFC 3084]	IETF RFC 3084 (2001), COPS Usage for Policy Provisioning (COPS-PR).

[IETF RFC 3159]	IETF RFC 3159 (2001), Structure of Policy Provisioning Information (SPPI).

[IETF RFC 3318]	IETF RFC 3318 (2003), Framework Policy Information Base.

[IETF RFC 4001]	IETF RFC 4001 (2005), Textual Conventions for Internet Network Addresses.

# 3	Definitions

## 3.1	Terms defined elsewhere

This Recommendation uses the terms Client Handle as defined in [IETF RFC 2748] and Policy Information Base (PIB) as defined in [IETF RFC 3084]. It uses the terms Transport Resource Control Physical Entity (TRC-PE) and Transport Physical Entity (T-PE) as defined in ITU-T Rec. Q.3300.

## 3.2	Terms defined in this Recommendation

This Recommendation defines the following term:

### 3.2.1	Session:

The term "session" is used in this document to refer to a COPS signalling relationship established between the TRC-PE acting in the role of a COPS Policy Decision Point (PDP) and the T-PE of acting in the role of a COPS Policy Enforcement Point (PEP).

# 4	Abbreviations and acronyms

This Recommendation uses the following abbreviations:

COPS				Common Open Policy Service

COPS-PR			COPS usage for policy provisioning

DEC				COPS DECision message

DEC Install			COPS DECision Install message

DEC Remove			COPS DECision Remove message

Diffserv			Differentiated Services model

DRE				Data Relay Entity

MPLS 				MultiProtocol Label Switching

PDP				Policy Decision Point

PEP				Policy Enforcement Point

PIB 				Policy Information Base

PRC				Provisioning Class

PRI				PRovisioning Instance

QoS 				Quality of Service

REQ 				COPS REQuest message

RPT 				COPS RePorT state message

T-PE				Transport Physical Entity

TRC-PE			Transport Resource Control Physical Entity

VSWITCH			Virtual SWITCHing

# 5	Protocol

This variant of the Rc Stage 3 definition uses the COPS protocol, and in particular the COPS-PR procedures and data models defined in [IETF RFC 3084].

The COPS protocol is a request/response protocol intended to operate in the Client/Server mode. The T-PE serves as the Policy Enforcement Point (PEP) and Client and the TRC-PE as the Policy Decision Point (PDP) and Server.

COPS implementations supporting this Recommendation shall support the COPS client type 0x800d (ITUT-RcPIB) and shall support the PIB defined in Annex A.

# 6	Procedures

## 6.1	Establishment of the COPS session

The T-PE shall initiate a TCP connection and open a COPS session with the TRC-PE as described in [IETF RFC 2748]. To establish an Rc session, the T-PE shall send a Client-Open message with the client identifier 0x800d (ITUT-RcPIB). The TRC-PE shall respond with a Client-Accept message for that client type. State synchronization may proceed as described in sections 2.5 of [IETF RFC 2748] and 3.1 of [IETF RFC 3084]. The client handle within the REQ message is of local significance to the T-PE. This Recommendation does not specify use of a ClientSI object within the Client-Accept message.

## 6.2	COPS session maintenance and termination

The T-PE and TRC-PE shall use the Keep-Alive procedures defined in [IETF RFC 2748] to ensure the continued availability of the COPS session. The session shall be terminated only by the loss of availability of one of the peers through failure or management action.

## 6.3	Provision of policy by the TRC-PE

The TRC-PE shall provide policy to the T-PE to indicate what information the TRC-PE wishes to acquire, using the contents of Named Decision objects within COPS-PR DEC messages. A DEC message must be returned in response to a REQ message from the T-PE. The TRC-PE may also send further DEC messages as required to modify previously set policy or collect additional information on a one-time basis.

Details are provided in Annex A, clause A.2.

## 6.4	Generation of reports by the T-PE

The T-PE shall provide information to the TRC-PE as determined by the policy installed by the DEC messages it receives. This information is provided within instances of the Named ClientSI object within COPS Report-State (RPT) messages.

Again, details are given in Annex A, clause A.2.

# 7	Application of Policy information Base (PIB)

## 7.1	Role of PIB

The Policy Information Base (PIB) provides a means to interwork between different product vendors. The PIB defines a collection of Provisioning Classes (PRC) which can be used by COPS to request or pass  data instances (PRIs) for any given data structure (PRC). Instances of the policy classes (PRIs) are each identified by a Provisioning Instance Identifier (PRID) in the PIB. (A PIB is just like a virtual database of the PRC.)

Here we define a PIB and inherit part of the data definitions from other PIBs, including PIBs in [IETF RFC 3159], [IETF RFC 3318], and [IETF RFC 4001].

## 7.2	Encoding of PIB

ASN.1 BER shall be used to encode the Provisioning Instance Identifier (PRID) and policy data as described in clause 2.2.1 of [IETF RFC 3084].

## 7.3	Definition of PIB

See Annex A, clauses A.1 and A.3 for details.

# 8	Reference to functional architecture

## 8.1	ITU-T Recommendation Y.2111

The protocol which the present document defines operates across the Rc reference point as defined in [ITU-T Y.2111].  This reference point is shown in Figure 1 (Figure 5 of [ITU-T Y.2111]).

Figure 1 – Position of the Rc reference point within the RACF architecture

# 9	Security Considerations

There may be several possible security threats at the Rc interface, such as denial of service, message disclosure by unauthorized snooping, and unauthorized message creation and modification.

In general, an attacker can surreptitiously intercept information, attempt to create unauthorized information, and send modified, reordered information or both.

There may be a risk that an attacker  impersonate a COPS server and illicitly acquire and tamper with the information. Even though the information is encrypted, a reply attack is possible.

The COPS protocol specification [IETF RFC 2748] requires all implementations to support use of an Integrity Object to prevent third-parties from acquiring and tampering. This Integrity Object consists of an HMAC Digest over the contents of the message. Its use requires a shared secret (key) available to the client and server.

Deployments which use the Integrity Object are required to have a means to manage the exchange of keys. However, the Integrity Object does not resolve all of the threats identified above, and in particular does not provide confidentiality.

Two reasonable means are available to satisfy the requirements for confidentiality and authentication:first is the use of IPSEC and, second is the use of Transport Layer Security (TLS). The use of one of these transports is strongly recommended in any deployment of the protocol documented in this Recommendation. Use of both IPSEC with encryption enabled and TLS on the same connection is a wasteful use of processing resources and must be avoided for that reason.

Annex A (Normative)

Policy Information Base

# A.1	Static Description of the PIB

The ITUT-RcPIB consists of six Provisioning Classes (PRCs) grouped into larger classes.  The RcResourceInfoClasses group contains four PRCs:

–	RcMPLSLabelTable, which provides a linked list of MPLS label objects;

–	RcMPLSInfoTable, which provides the following information for individual Label Switched Paths (LSPs):

–	active/inactive status

–	by reference, the label value

–	next-hop IP address

–	RcDreInterfaceTable, which provides the active/inactive status and interface name for interfaces on non-MPLS data relay entries (e.g., VSwitches);

–	RcResourceManageTable, which the TRC-PE uses to request status reports.

The second major group of PRCs is the RcServiceReportClasses group.  This group may be expanded in the future, but at the moment contains only a single sub-group, RcServiceReportClasses.  RcServiceReportClasses contains two PRCs:

–	RcStateReportTable, which indicates the success or failure of a particular query and may provide diagnostic information in the case of failure;

–	RcOverloadReportTable, which can be used to indicate that the T-PE is overloaded or has recovered from overload.

# A.2	Usage

To query the status of a specific MPLS LSP, the TRC-PE places an RcResourceManageTable entry instance into a DEC install request, with the value of the  RcResourceManageContent attribute pointing to a specific entry of the RcMPLSInfoTable.  In response, the T-PE generates a RPT message into which it places:

– 	an RcStateReportTable entry instance indicating whether the query was processed successfully;

– 	in the case of success:

–	the RcMPLSInfoTable entry instance to which the RcResourceManageTable entry instance pointed, with the appropriate values filled in;

–	except where the status of the  RcMPLInfoTable entry instance was "not exist", the RcMPLSLabelTable entry instance to which the RcMPLSInfoMPLSLabel attribute points, giving the value of the path label;

–	in the case where the previous query failed because of overload, an  RcOverloadReportTable entry instance indicating recovery.

– 	in the case of failure where the failure is due to overload of the T-PE, an  RcOverloadReportTable entry instance indicating overload.

To acquire the status of every MPLS path supported by the T-PE, the TRC-PE should begin by requesting the status of the RcMPLSInfoTable entry with instance value equal to 1.  This entry may or may not exist, as indicated by the returned RcMPLSInfoMPLSStatus attribute value.  If it does not exist, the value of the RcMPLSInfoNext attribute returned by the T-PE shall point to the first valid RcMPLSInfoTable entry instance, thus giving the TRC-PE a starting point for walking through the complete table.

Similar operations apply to the retrieval of status for Data Relay Entity interfaces.

# A.3	Rc Policy Information Base

ITUT-RcPIB  PIB-DEFINITIONS ::= BEGIN

IMPORTS

Unsigned32, Integer32, MODULE-IDENTITY,

MODULE-COMPLIANCE, OBJECT-TYPE, OBJECT-GROUP

FROM COPS-PR-SPPI            -- Defined in [IETF RFC 3159]

InstanceId, Prid

FROM COPS-PR-SPPI-TC         -- Defined in [IETF RFC 3159]

zeroDotZero               FROM SNMPv2-SMI  -- [IETF RFC 2578]

InetAddress, InetAddressType,

InetAddressPrefixLength

FROM INET-ADDRESS-MIB;       -- Defined in [IETF RFC 4001]

ITUT-RcPib MODULE-IDENTITY

SUBJECT-CATEGORIES   { ITUT-Rc(0x800D) } – ITU-T Rc COPS Client Type

LAST-UPDATED "200709170000Z"

ORGANIZATION "ITU-T Study Group 11"

CONTACT-INFO

"XUE LiLi

Huawei Technology Co. Ltd.

E-mail: xuelili@huawei.com"

DESCRIPTION

"A PIB module containing the set of provisioning

classes that are required for support of policies for

Rc Cops interface"

REVISION "200709170000Z"

DESCRIPTION

"The Rc PIB for Rec. Q.3304.1 version 1"

::= { 0.0.17.3304.127.1.2.0 }

-- itu-t(0) recommendation(0) q(17) q3304(3304) hyphen(127) <...>(1)

--  pib(2) version1 (0)

RcResourceInfoClasses           OBJECT IDENTIFIER ::= { ITUT-RcPIB 1}

RcServiceEventClasses           OBJECT IDENTIFIER ::= { ITUT-RcPIB 2}

RcServiceReportClasses          OBJECT IDENTIFIER ::= { RcServiceEventClasses 1}

---------------------------------------------------------

--  RcMPLSLabelTable Table

--  Lsp Label PRC

RcMPLSLabelTable OBJECT-TYPE

SYNTAX         SEQUENCE OF RcMPLSLabelEntry

PIB-ACCESS     install

STATUS         current

DESCRIPTION

"This table represents the Rc label."

::= { RcResourceInfoClasses 1 }

RcMPLSLabelEntry OBJECT-TYPE

SYNTAX         RcMPLSLabelEntry

STATUS         current

DESCRIPTION

"LSP"

PIB-INDEX { RcMPLSLabelPrid }

UNIQUENESS { }

::= { RcMPLSLabelTable 1 }

RcMPLSLabelEntry ::= SEQUENCE {

RcMPLSLabelPrid                          InstanceId,

RcMPLSLabelValue                         Unsigned32,

RcMPLSLabelNext                          Prid

}

RcMPLSLabelPrid OBJECT-TYPE

SYNTAX         InstanceId

STATUS         current

DESCRIPTION

"An arbitrary integer index that uniquely identifies an

instance of the RcMPLSLabel class."

::= { RcMPLSLabelEntry 1 }

RcMPLSLabelValue OBJECT-TYPE

SYNTAX         Unsigned32

STATUS         current

DESCRIPTION

"The label value for this path"

::= { RcMPLSLabelEntry 2 }

RcMPLSLabelNext OBJECT-TYPE

SYNTAX         Prid

STATUS         current

DESCRIPTION

"References the next of a list RcMPLSLabel instance.

A value of zeroDotZero indicates end of the list. "

DEFVAL  { zeroDotZero }

::= { RcMPLSLabelEntry 3 }

---------------------------------------------------------------

-- This table is used for MPLS query or report

--

RcMPLSInfoTable OBJECT-TYPE

SYNTAX         SEQUENCE OF RcMPLSInfoEntry

PIB-ACCESS     install

STATUS         current

DESCRIPTION

"This table represents the Rc Query Label.

::= { RcResourceInfoClasses 2}

RcMPLSInfoEntry OBJECT-TYPE

SYNTAX         RcMPLSInfoEntry

STATUS         current

DESCRIPTION

"LSP state"

PIB-INDEX { RcMPLSInfoPrid }

UNIQUENESS { }

::= { RcMPLSInfoTable 1 }

RcMPLSInfoEntry ::= SEQUENCE {

RcMPLSInfoPrid                 InstanceId,

RcMPLSInfoMPLSStatus           INTEGER,

RcMPLSInfoMPLSLabel            Prid,

RcMPLSInfoCnIpAddrType         InetAddressType,

RcMPLSInfoCnIpAddr             InetAddress,

RcMPLSInfoNext                 Prid

}

RcMPLSInfoPrid OBJECT-TYPE

SYNTAX         InstanceId

STATUS         current

DESCRIPTION

"An arbitrary integer index that uniquely identifies an

instance of the RcMPLSInfo class."

::= { RcMPLSInfoEntry 1 }

RcMPLSInfoMPLSStatus OBJECT-TYPE

SYNTAX         INTEGER {

active (0),

inactive (1),

not exist(0xFF)

STATUS         current

DESCRIPTION

"The label status, describe the status of LSP label."

::= { RcMPLSInfoEntry 2 }

RcMPLSInfoMPLSLabel OBJECT-TYPE

SYNTAX         Prid

STATUS         current

DESCRIPTION

" It is referenced the RcMPLSLabelValue  of the

RcMPLSlable class."

::= { RcMPLSInfoEntry 3 }

RcMPLSInfoCnIpAddrType OBJECT-TYPE

SYNTAX         InetAddressType

STATUS         current

DESCRIPTION

"Cn IP address type."

::= { RcMPLSInfoEntry 4 }

RcMPLSInfoCnIpAddr OBJECT-TYPE

SYNTAX         InetAddress

STATUS         current

DESCRIPTION

""

::= { RcMPLSInfoEntry 5 }

RcMPLSInfoNext OBJECT-TYPE

SYNTAX         Prid

STATUS         current

DESCRIPTION

"References the next of a list RcMPLSInfoinstances.

A value of zeroDotZero indicates end of the list."

DEFVAL  { zeroDotZero }

::= { RcMPLSInfoEntry 6 }

---------------------------------------------------------

--  Dre interface PRC

RcDreInterfaceTable OBJECT-TYPE

SYNTAX         SEQUENCE OF RcDreInterfaceEntry

PIB-ACCESS     install

STATUS         current

DESCRIPTION

"This table represents the Rc Dre Interface.

"

::= { RcResourceInfoClasses 3 }

RcDreInterfaceEntry OBJECT-TYPE

SYNTAX         RcDreInterfaceEntry

STATUS         current

DESCRIPTION

"Dre Interface"

PIB-INDEX { RcDreInterfacePrid }

UNIQUENESS { }

::= { RcDreInterfaceTable 1 }

RcDreInterfaceEntry ::= SEQUENCE {

RcDreInterfacePrid                          InstanceId,

RcDreInterfaceStatus                        INTEGER,

RcDreInterfaceName                          OCTET STRING(SIZE (0..67)),

RcDreInterfaceNext                          Prid

}

RcDreInterfacePrid OBJECT-TYPE

SYNTAX         InstanceId

STATUS         current

DESCRIPTION

"An arbitrary integer index that uniquely identifies an

instance of the RcIterface  class."

::= { RcDreInterfaceEntry 1 }

RcDreInterfaceStatus OBJECT-TYPE

SYNTAX         INTEGER {

active (0),

inactive (1),

notExist(0xFF)

STATUS         current

DESCRIPTION

"The Dre interface status"

::= { RcDreInterfaceEntry 2 }

RcDreInterfaceName OBJECT-TYPE

SYNTAX         OCTET STRING(SIZE (0..67))

STATUS         current

DESCRIPTION

"The Interface Name."

::= { RcDreInterfaceEntry 3 }

RcDreInterfaceNext OBJECT-TYPE

SYNTAX         Prid

STATUS         current

DESCRIPTION

"References the next of a list RcDreInterface class.

A value of zeroDotZero indicates end of the list."

DEFVAL  { zeroDotZero }

::= { RcDreInterfaceEntry 4 }

-------------------------------------------------------------------------

--

-- Rc Resource Query Table

--

RcResourceManageTable OBJECT-TYPE

SYNTAX         SEQUENCE OF RcResourceManageEntry

PIB-ACCESS     install

STATUS         current

DESCRIPTION

"This table represents the Rc Resource Query.

::= { RcResourceInfoClasses 4 }

RcResourceManageEntry OBJECT-TYPE

SYNTAX         RcResourceManageEntry

STATUS         current

DESCRIPTION

"An instance of the RcResourceManage class"

PIB-INDEX { RcResourceManagePrid }

UNIQUENESS { }

::= { RcResourceManageTable 1 }

RcResourceManageEntry ::= SEQUENCE {

RcResourceManagePrid                 InstanceId,

RcResourceManageContent              Prid

}

RcResourceManagePrid OBJECT-TYPE

SYNTAX         InstanceId

STATUS         current

DESCRIPTION

"An arbitrary integer index that uniquely identifies an

instance of the RcResourceManage class."

::= { RcResourceManageEntry 1 }

RcResourceManageContent OBJECT-TYPE

SYNTAX         Prid

STATUS         current

DESCRIPTION

"Reference the instances of RcResourceInfoClasses, can be used

to query or report the resource state ."

::= { RcResourceManageEntry 2 }

---------------------------------------------------------------------

-- Rc DecResult Report Table

--

RcStateReportTable OBJECT-TYPE

SYNTAX         SEQUENCE OF RcStateReportEntry

PIB-ACCESS     notify

STATUS         current

DESCRIPTION

"The Rc Decsion Result Report PRC."

::= { RcServiceReportClasses 1 }

RcStateReportEntry OBJECT-TYPE

SYNTAX         RcStateReportEntry

STATUS         current

DESCRIPTION

"An instance of the RcStateReport class."

PIB-INDEX { RcStateReportPrid }

UNIQUENESS { }

::= { RcStateReportTable 1 }

RcStateReportEntry ::= SEQUENCE {

RcStateReportPrid            InstanceId,

RcStateReportStatus          INTEGER,

RcStateReportDetails         Prid

}

RcStateReportPrid OBJECT-TYPE

SYNTAX         InstanceId

STATUS         current

DESCRIPTION

"An arbitrary integer index that uniquely identifies an

instance of the RcStateReport class."

::= { RcStateReportEntry 1 }

RcStateReportStatus OBJECT-TYPE

SYNTAX         INTEGER {

success (1),

failure (2),

usage   (3) }

STATUS         current

DESCRIPTION

"When Status is:

success: Indicates the successful implementation of the

decision.

RcStateReportDetails:

References nothing otherwise (contains the value

zeroDotZero).

Failure: Indicates the failure of implementing the decision.

RcStateReportDetails may references an Error object,

or may have the value zeroDotZero when no error

object is needed, in which case COPS and COPS-PR

error codes and error objects are sufficient.

Usage:   RcStateReportDetails references an instance of

frwkBasePibClasses class."

::= { RcStateReportEntry 2 }

RcStateReportDetails OBJECT-TYPE

SYNTAX         Prid

STATUS         current

DESCRIPTION

"May reference an instance of frwkBasePibClasses(frwkErrorTable)

or may have the value of zeroDotZero depending on the value of

RcStateReportStatus."

::= { RcStateReportEntry 3 }

--

-- Rc  Overload Report Table

--

RcOverloadReportTable OBJECT-TYPE

SYNTAX         SEQUENCE OF RcOverloadReportEntry

PIB-ACCESS     install

STATUS         current

DESCRIPTION

"This table represents the Rc overload information.

"

::= { RcServiceReportClasses 2 }

RcOverloadReportEntry OBJECT-TYPE

SYNTAX         RcOverloadReportEntry

STATUS         current

DESCRIPTION

"Overload information"

PIB-INDEX { RcOverloadReportPrid }

UNIQUENESS { }

::= { RcOverloadReportTable 1 }

RcOverloadReportEntry ::= SEQUENCE {

RcOverloadReportPrid                      InstanceId,

RcOverloadReportStatus                    INTEGER

}

RcOverloadReportPrid OBJECT-TYPE

SYNTAX         InstanceId

STATUS         current

DESCRIPTION

"An arbitrary integer index that uniquely identifies an

instance of the Report Overload class."

::= { RcOverloadReportEntry 1 }

RcOverloadReportStatus OBJECT-TYPE

SYNTAX         INTEGER {

overload(0),

recover(1)

}

STATUS         current

DESCRIPTION

"Overload status."

::= { RcOverloadReportEntry 2 }

END

_____________________