Broadband Forum Liaison To:

IETF Statements, statements@ietf.org 
David Sinicrope, IETF Liaison Manager, david.sinicrope@ericsson.com

From:

Christophe Alter
Broadband Forum Technical Committee Chair 
(christophe.alter@orange.com)

Liaison Communicated By:

Ken Ko

ken.ko@adtran.com

Date: March 8, 2013

Subject: Performance Measurements Architecture

The Broadband Forum would like to share the current status and thinking of its efforts related to performance measurement. There are coordinated efforts underway in multiple Broadband Forum working groups under the umbrella project of WT-304 “Broadband Access Service Attributes and Performance Metrics”.

Four high-level functions related to the operation and management of measurement functionality have been identified. These are:  the Measurement Agent, Measurement Controller, Data Collector, and Management Server. The Measurement Controller may further be split into a Scheduling function and Test Admission function. These functions are defined as follows:

| Data Collector | An operational function that collects measurement data from a Measurement Agent. |
| --- | --- |
| Management Server | Manages and configures a physical device or network element. Examples include a TR-069 ACS (Auto-Configuration Server), or an EMS (Element Management System). |
| Measurement Agent | An operational function that contains one or more Measurement functions. |
| Measurement Controller | An operational function that controls running, scheduling, and general coordination of Measurement functions within a Measurement Agent. |

1.	The Management Server configures a Measurement Agent (MA) to communicate with a specific Measurement Controller (e.g., TR-069 server may configure parameters in a managed CE router’s Measurement Agent).

2.	The Measurement Controller configures the MAs with specific tests (e.g., the Measurement Controller may schedule periodic tests for the MA to run).  Includes attributes such as target MA, type of test, and destination for results. If a particular test requires the MA to determine availability of the target MA, the Measurement Controller may include a Test Admission function to support this determination.

3.	The MAs run the tests (e.g., runs a throughput or latency test).

4.	MAs send results to the Data Collector(s) (e.g., the results are sent to the designated collection function).  Both agents can send results.

Below is a diagram that shows an example of how these functions may be used to configure and coordinate single domain and cross domain testing.

During a discussion on the Test Admission function, it was suggested that SIP may be used to provide an inter (and intra) domain mechanism to determine test target resource availability, prior to performing a test against a target. We would be curious to learn the thoughts of IETF members on this topic. If there is interest in this, and IETF would like to pursue work in this area, BBF would gladly defer to IETF in this matter.

BBF also discussed service attributes and mechanisms for a service provider to provide these attributes to Measurement Agents inside the home network that are not affiliated with the service provider. One idea that surfaced was that the service provider could provide service attributes to a service-provider-managed device inside the home network, and that managed device could expose the service attributes via an xml-formatted page. This page could be discovered using DNS-SD (RFC6763), and potentially advertised using mDNS (RFC6762). We would be curious to learn thoughts of IETF members on this topic, as well.

We would like to encourage IETF efforts to define information models for test and report parameters, as we believe these would be very valuable to our efforts. We look forward to continuing to work with IETF on the topic of performance measurements.

Sincerely,

Christophe Alter,

Broadband Forum Technical Committee Chair

CC:

Christophe Alter, Broadband Forum Technical Committee Chair (christophe.alter@orange.com)

Robin Mersh, Broadband Forum CEO (rmersh@broadband-forum.org)

Gabrielle Bingham, Broadband Forum Secretariat (gbingham@broadband-forum.org)

Jason Walls, Broadband Home Working Group Co-Chair (jason@qacafe.com)

John Blackford, Broadband Home Working Group Co-Chair (john.blackford@pace.com)

Dave Thorne BT Broadband Forum E2E Architecture WG Chair (david.j.thorne@bt.com)

Dave Allan Ericsson Broadband Forum E2E Architecture WG Chair (david.i.allan@ericsson.com)

Sven Ooghe Alcatel-Lucent Broadband Forum E2E Architecture WG Vice Chair (sven.ooghe@alcatel-lucent.com)

Peter Adams, Broadband Forum, Operations and Network Management Technical WG Chair (peter.adams@adtran.com)

Brian Trammell, IP Performance Metrics WG Chair (trammell@tik.ee.ethz.ch)

Bill Cerveny, IP Performance Metrics WG Chair (bill@wjcerveny.com)

Dan Romascanu, Large-Scale Measurement of Broadband Performance BOF Chair (dromasca@avaya.com)

Al Morton, Large-Scale Measurement of Broadband Performance BOF Chair (acmorton@att.com)

Date of Upcoming Broadband Forum Meetings

| DATES | LOCATION |
| --- | --- |
| 3rd – 7th June, 2013 | Nanjing, China |
| 16th – 20th September, 2013 | Atlanta, Georgia, USA |
| 18th – 22nd November, 2013 | Rome, Italy |

Note: A list of upcoming meetings can be found at http://www.broadband-forum.org/meetings/upcomingmeetingsataglance.php