3GPP TSG CT WG4 Meeting #85bis	C4-185491

Sophia Antipolis, France, 9th – 13th July 2018

Title:	LS OUT on User Plane Analysis

Response to:

Release:	Release-16

Work Item:	FS_UPPS

Source:	CT4

To:	IETF DMM

Cc:

Contact Person:

#### Name:	Sridhar Bhaskaran, Huawei Technologies

Tel. Number:	+91-98862 50226

E-mail Address:	sridhar.bhaskaran@huawei.com

Send any reply LS to:	3GPP Liaisons Coordinator, mailto:3GPPLiaison@etsi.org

Attachments:	None

1. Overall Description:

CT4 reviewed the IETF draft-hmm-dmm-5g-uplane-analysis-00 based on the input discussion paper submitted to CT4 in C4-185292. CT4 thanks IETF DMM for their analysis. CT4 would like to provide the following initial feedback on the same. CT4 intends to do further analysis and provide any additional feedback, if any, in future. CT4 would like to emphasize that the evaluation criteria for the user plane protocol study (FS_UPPS) in 5GC shall be defined by 3GPP CT4 and the work has just now started in 3GPP.

.

| Sl.No | Section and Text From IETF draft-hmm-dmm-5g-uplane-analysis-00 | Comment |
| --- | --- | --- |
| 1 | Section 3.1 Figure 1 and Figure 2 | This representation is not accurate. From 3GPP point of view the inner IPv4/IPv6 together with its upper layer data is called the PDU. See figure 8.3.1-1 of TS 23.501. |
| 2 | Section 3.1 [GTP-U-4]: UDP zero checksum is not available in case of IPv6 transport. | CT4 thanks IETF DMM for highlighting the availability of a later RFC 8200. While it is true that introducing support for UDP zero checksum with IPv6 underlying transport in later release of 3GPP may need to consider interoperability issues, CT4 would like to highlight that solutions for handling such issues can be identified by 3GPP CT4 (E.g Negotiation of UPF feature capabilities via control plane) |
| 3 | Section 3.1 [GTP-U-5]: GTP-U does not support to response ICMP PTB for Path MTU Discovery. "Unnecessary fragmentation should be avoided" is recommended and to avoid the fragmentation operator should configure MTU size at UE [TS.29.281-3GPP]. However, there's no reference and specification of Path MTU Discovery for IPv6 transport. If encapsulated IPv6 packet is too big on a network link between tunnel endpoint nodes, UE may not receive ICMPv6 Packet Too Big message and causes Path MTU Discovery black hole. and Section 5.3: The expected evaluation points from this aspect should be that the candidate protocols are able to dynamically adjust path MTU size with appropriate MTU size discovery mechanism. It also should be that how the candidate protocols leverage IPv6 to deal with header size increasing. | Clause 4.2.2 of 3GPP TS 29.281 states Recommendations on how to set the default inner MTU size at the PDN GW and UE/MS to avoid IP fragmentation of both inner IP packets (in the PDN GW or UE/MS) and outer IP packets in the backbone are specified in clause 9.3 of 3GPP TS 23.060 [4]. And clause 9.3 of 3GPP TS 23.060 states The PDP PDUs shall be routed and transferred between the MS and the GGSN or P-GW as N-PDUs. In order to avoid IP layer fragmentation between the MS and the GGSN or P-GW, the link MTU size in the MS should be set to the value provided by the network as a part of the IP configuration. The link MTU size for IPv4 is sent to the MS by including it in the PCO (see TS 24.008 [13]). The link MTU size for IPv6 is sent to the MS by including it in the IPv6 Router Advertisement message (see RFC 4861 [98]). The MTU between RAN and the P-GW or UPF is discovered by offline means and the operator takes into account the MTU that is transferrable on the radio interface and based on this the operator configures the right MTU to be used. This is then signalled to the UE either via PCO (for IPv4 case) or the IPv6 RA message (for IPv6 case). Hence for the uplink transfer the UE is aware of the link MTU (at least the recommended MTU for 3GPP link). See also Annex C of 3GPP TS 23.060 where link MTU considerations for the UE when GTPU tunnelling over IPv6 is done is explained. |
| 4 | [GTP-U-6]: Supports sequence number option and sequence number flag in the header, but it is not recommended to be used by most GTP-U entities. | In 3GPP, the in sequence delivery is required only during handover procedure. The in sequence delivery is used by the RAN entities only, to ensure to transmit packets in the correct order when forwarding packets from the source to the target. For other scenarios, the in sequence delivery is not needed as applicable protocol (as payload of GTP-U, e.g. TCP) address that. |
| 5 | Section 3.2 [GTP-U-8]: GTP-U supports DSCP marking based on the QFI. DSCP marking on outer IPv4 or IPv6 shall be set by sender tunnel endpoint node based on the QFI. This specification is described in section 4.4.1 of [TS.29.281-3GPP]. However in [TS.29.281-3GPP] "DSCP marking based on QCI" is specified but "DSCP marking based on QFI" has not been noted. To support QFI of 5G QoS framework, it seems to need to update [TS.29.281-3GPP]. | CT4 thanks IETF DMM for this observation. CT4 has taken note of it and intends to update the specification accordingly. Also this is a system level feature and not a protocol level feature. This has been specified by SA2 but CT4 has not yet aligned the protocol change. |
| 6 | Section 3.2 [GTP-U-9]: GTP-U does not specify extension header order. | CT4 would like IETF DMM to kindly refer the following NOTE under Figure 5.2.1-3 of the latest 3GPP TS 29.281 (V15.3.0) as of June 2018 NOTE 4: For a G-PDU with several Extension Headers, the PDU Session Container should be the first Extension Header. Since the PDU Session Container has information that is essential for faster processing and forwarding of the data (e.g QFI), it is recommended to be included as the first extension header. |
| 7 | [GTP-U-10]: Does not support an indication of next-header type. | Since GTP-U is a tunnelling protocol and the entire payload of GTP-U is treated as a PDU to be transferred by the RAN to the UE (for downlink direction) or to be routed from PDU Session Anchor UPF to the DN (for uplink direction), there is no need for identifying the type of payload. |
| 8 | Section 4.2 ARCH-Req-5: No limitation for number of UPFs in a data path Putting multiple UPFs, which provides specific function, in a data path enables flexible function deployment to make sure load distribution optimizations, etc. | While it is true that 3GPP does not constrain the number of UPFs in a data path, CT4 would like to highlight to IETF DMM that all UPFs that are in the data path shall be controlled by an SMF and hence shall have an N4 interface. |
| 9 | Section 5.2 Supporting MP2P data path by GTP-U could be a gap in terms of single PDU session multi-homing, since GTP-U is a point-to-point tunneling protocol as it is described in Section 3. | CT4 would like to highlight IETF DMM that GTP-U allows the same F-TEID be used as the destination tunnel endpoint for tunnels from multiple sources. For example: 1. Even In EPC, in Tracking Area Update procedure with SGW change and data forwarding there is already a use case where the eNB exposes single FTEID for receiving downlink data from 2 source end points (new and old SGWs). See clause 5.3.3.1A of 3GPP TS 23.401 step 12, 14 and 15. The F-TEID is the F-TEID for the indirect forwarding received from step 13 or it may be the F-TEID of the eNB (when eNB supports forwarding). The support for using the same FTEID as destination FTEID also applies for 5G as given below in the 5G use cases. 2. Dual connectivity in 5G system where the Master and Slave gNB can use the same uplink FTEID of the UPF for uplink traffic of the same PDU session. 3. For the IPv6 multihoming case, the downlink traffic from multiple PDU Session Anchors of the same PDU session may use the same N9 F-TEID of the branching point UPF. CT4 intends to clarify these aspects in 3GPP TS 29.281. |
| 10 | Section 5.6 As similar with QoS flow lookup described in Section 5.5, UPFs along the path are repeatedly detecting an specified traffic flow in inner PDU. It could increase redundant flow detection load on every UPFs that could be avoided if the upstream UPF put some identifier which abstracts the detected flow into the packets. It enables following UPFs just find the ID to detect the indicated flow from the packet. | CT4 would like to highlight that there is no requirement in 3GPP to do repeated inner packet based classification in every UPF along the packet path of a PDU session. PDU based classification happens at PSA UPF. Intermediate UPFs operate based on TEIDs and QFI which is assumed to exist in the first extension header, as they are required to only forward the packets. |
| 11 | Section 5.7 That's just one way for network slicing, but it helps to reduce the operational burden while there's no 3GPP specification for slice lifecycle managements, such as create, update, and delete operations for slices. | CT4 would like to point out the following 3GPP specifications that specify slice lifecycle management a. 3GPP TS 28.530 - Management and orchestration of networks and network slicing; Concepts, use cases and requirements b. 3GPP TS 28.531 - Management and orchestration of networks and network slicing; Provisioning; Stage 1 c. 3GPP TS 28.532 - Management and orchestration of networks and network slicing; Provisioning; Stage 2 and stage 3 d. 3GPP TS 28.533 - Management and orchestration of networks and network slicing; Management and orchestration architecture |

2. Actions:

To IETF DMM Group.

ACTION:

CT4 kindly requests IETF DMM to take the above initial feedback into consideration.

3. Date of Next CT and CT4 Meetings:

CT4#86	20th – 24th Aug 2018	West Palm Beach, US

CT#81	10th - 11th Sep 2018	Gold Coast, Australia

CT4#86bis	15th - 19th Oct 2018	Vilnius, Lithuania