# 3GPP TSG SA Meeting #87E	SP-200095

# 17-20 March 2020, Electronic meeting	(revision of SP-190558)

Source:	SA WG2

Title:	Revised SID: Study on Access Traffic Steering, Switch and Splitting support in the 5G system architecture Phase 2

Document for:	Approval

Agenda Item:	6.5

Work Item:	FS_ATSSS_Ph2

3GPP TSG SA2 Meeting#137e	S2-2002593

Elbonia Feb. 24 - 27, 2020	(revision of S2-2001952)

3GPP™ Work Item Description

For guidance, see 3GPP Working Procedures, article 39; and 3GPP TR 21.900.
Comprehensive instructions can be found at http://www.3gpp.org/Work-Items

# Title:	Study on Access Traffic Steering, Switch and Splitting support in the 5G system architecture Phase 2

## Acronym: FS_ATSSS_Ph2

## Unique identifier:	840084

## 1	Impacts

| Affects: | UICC apps | ME | AN | CN | Others (specify) |
| --- | --- | --- | --- | --- | --- |
| Yes |  | X |  | X |  |
| No |  |  | X |  |  |
| Don't know | X |  |  |  | X |

## 2	Classification of the Work Item and linked work items

### 2.1	Primary classification

This work item is a ….

|  | Feature |
| --- | --- |
|  | Building Block |
|  | Work Task |
| X | Study Item |

### 2.2	Parent Work Item

| Parent Work Items |
| --- |
| Unique ID | Title |

### 2.3	Other related Work Items and dependencies

{List here other Work Items which relate to the proposed one but are not part of the hierarchical structure.}

| Other related Work Items (if any) |
| --- |
| Unique ID | Title | Nature of relationship |
| 820021 | Access Traffic Steering, Switch and Splitting support in the 5G system architecture | Release 16 ATSSS work item. |

## 3	Justification

The ATSSS feature is to enable UEs that can be simultaneously connected to both 3GPP access and non-3GPP access. The 5G system should be able to take advantage of these two accesses in a way that improves the user experience, optimizes the traffic distribution across two accesses, enables the provision of new high-data-rate services, etc.

During the Release-16 study and normative development of ATSSS, certain aspects of the initial scope such as traffic splitting support for GBR traffic, more advanced steering modes, additional steering methods, certain roaming scenarios that were not supported in Rel-16, and several other potential performance enhancement procedures have been deferred for further study.

The intent of this SID is to study some of the deferred features and an additional access deployment scenario as described below.

## 4	Objective

The objective of this SID is to further investigate the following aspects for UEs that can connect to 5GC over both 3GPP and non-3GPP accesses:

-	Whether and how to support additional steering mode(s), with potential PMF extensions as needed.

-	Whether and how to support additional steering methods(s). Proposed solutions shall be based on IETF protocols or extension of such protocols (i.e. QUIC/MP-QUIC).

- Whether and how to support multi-access PDU session with one access leg over EPC and the other access leg over non-3GPP access 5GS.

This study may also extend the policies to support the above extensions.

This study is based on the 5GS Release-16 ATSSS normative work including the policy management support. Similar procedures that may be applied in the 5G RAN are outside the scope of this study.

This study is restricted only to ATSSS support for traffic routed over one 3GPP access and one non-3GPP access. Usage of ATSSS for traffic routed over multiple 3GPP accesses is outside the scope of this study.

5	Expected Output and Time scale

| New specifications {One line per specification. Create/delete lines as needed} |
| --- |
| Type | TS/TR number | Title | For info at TSG# | For approval at TSG# | Remarks |
| Internal TR | 23.700-93 | Study on Access Traffic Steering, Switch and Splitting support in the 5G system architecture Phase 2 | TSG#88 (June 2020) | TSG#88 (June 2020) | So, Tricci, ZTE, tso@ztetx.com |

{Note 1: Only TSs may contain normative provisions. Study Items shall create or impact only TRs.
"Internal TR" is intended for 3GPP internal use only whereas "External TR" may be transposed by OPs.}

{Note 2: The first listed Rapporteur is the specification primary Rapporteur. Secondary Rapporteur(s) are possible for particular aspect(s) of the TS/TR. In this case, their responsibility has to be provided as "Remarks".}

| Impacted existing TS/TR {One line per specification. Create/delete lines as needed} |
| --- |
| TS/TR No. | Description of change | Target completion plenary# | Remarks |

## 6	Work item Rapporteur(s)

So, Tricci, ZTE, tso@ztetx.com

## 7	Work item leadership

SA2

8	Aspects that involve other WGs

No

9	Supporting Individual Members

Supporting IM name

ZTE

ETRI

Motorola Mobility

Lenovo

Broadcom

Interdigital

Convida Wireless

LG Electronics

Huawei

Deutsche Telekom

Nokia

Nokia Shanghai Bell

Thales

Orange

Apple

BT

Telecom Italia

Ruckus

CommScope Technologies

HPE

Cisco Systems

Charter Communications

Rogers Communications

CableLabs

Matrixx