## Slide 1
OSPF Link Information Model for WSON
draft-schroetter-wson-ospf-link-info-00
Dirk Schroetter @ Cisco
Giovanni Martinelli @ Cisco
IEFT 77 - Anaheim
Notes: <number>

## Slide 2: Motivation
Propose a more granular approach compared to what currently available in WSON routing models.
  Allow Partition the link in wavelength sets
  Hint to RWA algorithm to associate wavelength to a certain set.
Provides some typical WSON Use-Case scenarios to we are trying to solve.
Goes in addition to current WSON proposal.
Notes: <number>

## Slide 3: Use case 1: Requires specific wavelengths on a given link
Client signals that require specific wavelengths on a given link
------------------------- ------+------------------
+------+ | +------+
L | WL 1 | L | | WL 1 |
+------+ | +------+
|
+------+ | +------+
I | WL 2 | I | | WL 2 | Sublink 1
+------+ | +------+ for 10G
|
+------+ | +------+
N | WL 3 | N | | WL 4 |
+------+ | +------+
+------------------
+------+ | +------+
K | WL 4 | K | | WL 3 | Sublink 2
+------+ | +------+ for 40G
------------------------- ------+------------------
Notes: <number>

## Slide 4: Use Case 2: Wavelengths reserved for specific uses
Usage Administrative Groups
E.g. AG=3 Only for backup purpose
------------------------- ------+------------------
+------+ | +------+
L | WL 1 | L | | WL 1 |
+------+ | +------+ Sublink 1
| for 10G
+------+ | +------+ with AG=1
I | WL 2 | I | | WL 2 |
+------+ | +------+
+------------------
+------+ | +------+
N | WL 3 | N | | WL 3 | Sublink 2
+------+ | +------+ for 40G AG=2
+------------------
+------+ | +------+
K | WL 4 | K | | WL 4 | Sublink 3
+------+ | +------+ for AG=3
------------------------- ------+------------------

## Slide 5: Use Case 3: Wavelength Availability based on adjacent channel usage
Wavelength assignment may depend on client signals already in places.
LINK SET 1
LINK SET 2
New Link Installed with spectrum constrain (e.g. 40g vs 10g channels)

## Slide 6: Link sub-TLVs definitions
Draft propose several sub-TLVs for the Link TLV.
    1. Sublink Wavelength Set
    2. Sublink Modulation Format Compatibility Set
    3. Signal Dependency Set
    4. Sublink Administrative Group

## Slide 7: 1. Sublink wavelength set
At least one wavelenth set must be defined for a sublink
Encoding allow using label set or bitmap as defined for wson
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Sublink ID | Encoding | Reserved |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
: Wavelength Descriptor :
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

## Slide 8: 2. Modulation Format Compatibility Set
Allow associate different modulation formats to a sublink
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Sublink ID | Encoding | Reserved |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Modulation Type 1 |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
: Modulation Type N :
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

## Slide 9: 3. Signal dependency Set
Indicate wavelength blocking within a sublink.
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Modulation Type |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|Grid | C.S | Lower Excursion |Grid | C.S | Upper Excursion |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

## Slide 10: 4. Sublink Administrative Group
Associate an Administrative Group with a sublink.
Same format as RFC3630
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Sublink ID | Reserved |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Administrative Group |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

## Slide 11: Comments?
THANK YOU!