## Slide 1: OSPF Extensions in support of O-E-O pools in GMPLS controlled all-optical networks draft-peloso-ccamp-wson-ospf-oeo-01
Pierre Peloso, Julien Meuric, Giovanni Martinelli

## Slide 2: Rationales for this work
Target: Flooding of information through OSPF-TE to provide a graph to compute both spatial and spectral assignment of a LSP into an all-optical meshed network (WSON).
Issues to solve: Not only flooding of wavelength availability inside links, but also:
  Switching constraints (spatial and spectral) inside nodes (between links)
  Description of O-E-O resources inside nodes (for regeneration or conversion purposes)
    Their availability
    Their features
    Their accessibility

## Slide 3: Summarizing table of information to be conveyed through IGP
Links related features
  Wavelength availability
Node related features
  physical switching constraints for node bypass static
  spectral switching constraints for node bypass static
  regenerators/converters availability dynamic
  regenerators/converters features static
    Signal features
    Wavelengths that can be handled
  regenerators/converters accessibility
    spatial static
    spectral dynamic
Next slides provide examples of architectures that illustrate the different node related features

## Slide 4: Fully flexible Y-node with 1 tunable and flexible pool of O-E-O
From node A
From node B
From node C
To node A
To node B
To node C
add
drop
…
…
Tun.
Drop
Tun.
Drop
OEO pool

## Slide 5: Partially Fixed ROADM
From node A
To node C
drop
Tun.
Drop
add
OEO pool

## Slide 6: Fully flexible Y node with 4 tunable pools of O-E-O fixed to links
From node A
From node B
From node C
To node A
To node B
To node C
Tun.
Drop
Tun.
Drop
Tun.
Drop
OEO pool 1
OEO pool 3
OEO pool 2
OEO pool 4

## Slide 7: Technical description of the OSPF-TE modifications
Provide an OSPF-TE layout that intrinsically separates some static info from some dynamic ones, exploiting the concept of OEO pools
  Have LSA for WDM links with availability of wavelength (dynamic)
  Have LSA for switching constraints of nodes (static)
  Have LSA for OEO resources (static and dynamic)
A
B
C
D
OEO pool
OEO pool
OEO pool

## Slide 8: Illustration of LSAs layout
A
C
D
A
C
D
OEO pool LSA
OEO pool LSA
Node B
LSA
Connectivity Matrix
Ingress ports
Egress ports
WDM links LSAs
WDM links LSAs

## Slide 9: LSA describing WDM links - referring to draft-zhang-ccamp-rwa-wson-routing-ospf-03
  Description of the fields of the Link TLV (top level TLV : type 2) within LSA type 1O (Opaque LSA) – Opaque Type 1 (TE-LSA)
      Link type rfc3630 1 Byte Pt-Pt or Pt-MPt
      Link ID rfc3630 4 Bytes IP Address of the egress node of the link
      Local interface IP address rfc3630 4 Bytes IP Address of the ingress node
      Remote interface IP address rfc3630 4 Bytes IP Address of the egress node of the link
      Traffic engineering metric rfc3630 4 Bytes TE value settable by operator
      Maximum bandwidth rfc3630 4 Bytes Maximum Bandwidth
      Unreserved bandwidth rfc3630 4 Bytes Unreserved Bandwidth
      Resource class/color rfc3630 4 Bytes Administrative value settable by operator
      Link Local/Remote Identifiers rfc4203 8 Bytes Two identifiers identifying interfaces at both ends of the link (values local to related node)
      Link Protection Type rfc4203 4 Bytes Describes the protection (usually unprotected)
      Shared Risk Link Groups (SRLGs) rfc4203 4N Bytes Group of common risks (e.g. same fiber duct)
      Interface Switch Cap Descriptor rfc3630, rfc4203 4N Bytes Describes the switch cap a priori LSC
      Wavelength restriction 4N Bytes Wavelength restriction
      Available wavelengths 4N Bytes Bitmap mask for available Wvl
      Shared Backup wavelengths 4N Bytes Bitmap mask for available Wvl

## Slide 10: LSA describing WDM nodes
  Description of the fields of the Node Attribute TLV (top level TLV : type 5) within LSA type 1O (Opaque LSA) – Opaque Type 4 (RI-LSA)
      Node Local Address draft-ietf-ospf-te-node-addr 4 Bytes Local IP Address of the node
      Connectivity Matrix 4N Bytes Description of connectivity constraints of the node, both spatial and spectral
  Connectivity matrix shall list interfaces of:
    Incoming and outgoing WDM links
    OEO pools

## Slide 11: LSA describing OEO resources
  Description of the fields of the Link TLV (top level TLV : type 3R) within LSA type 1O (Opaque LSA) – Opaque Type 1 (TE-LSA)
      Pool ID 4 Bytes ID of the Pool
      Traffic engineering metric rfc3630 4 Bytes TE value settable by operator
      Resource class/color rfc3630 4 Bytes Administrative value settable by operator
      Link Local/Remote Identifiers rfc4203 8 Bytes Two identifiers identifying interfaces at both ends of the link (values local to related node)
      Ingress Available wavelength 4N Bytes Bitmap mask for available Wvl to the pool
      Egress Available wavelength 4N Bytes Bitmap mask for available Wvl from the pool
      Ingress Transponder info Fixed ID and features of ingress side of a OEO device
      Egress Transponder info Fixed ID and features of egress side of an OEO device
      Shared Risk Link Groups (SRLGs) rfc4203 4N Bytes Group of common risks (e.g. same shelf)
  Transponder info shall describe the features of OEO devices and there shall be a list of those (as many instances as OEO devices in the pool). It contains a description of the features of a given device:
    Local Device ID
    Signal compatibility features (modulation format, bit-rate, etc…)
    Wavelength that can be handled by the device
  Need to get a new type of top TLV from IANA

## Slide 12: Conclusion
This draft presents a solution to address the flooding of information through OSPF-TE to provide a graph that can be exploited to compute both the spatial and spectral assignment of a LSP into WSON.
Next step: Get a CCAMP feedback on the content of this solution.

## Slide 13
Questions and discussion?