## Slide 1: OAM Configuration Framework and Technology Specific Extensions
draft-ietf-ccamp-oam-configuration-fwk
draft-ietf-ccamp-rsvp-te-eth-oam-ext
draft-ietf-ccamp-rsvp-te-sdh-otn-oam-ext
Attila Takacs (editor)
IETF-77 Anaheim

## Slide 2: Background, Motivation and Objectives
Extend GMPLS CP to configure OAM entities
  Useful for any GMPLS controlled transport network
  Also a requirement for MPLS-TP LSPs
Avoid two separate management/configuration steps: connection setup followed by OAM configuration
  Additional delay and processing
  Prune to missconfiguration errors
Need to extend RSVP-TE signaling
  Maintenance entity identification parameters (MEP/MIP)
  Configure OAM parameters (e.g., monitoring frequency)
  OAM control (e.g., admin down, disable/enable AIS)

## Slide 3: Documents structure – Update
draft-ietf-ccamp-oam-configuration-fwk
draft-ietf-ccamp-rsvp-te-eth-oam-ext
draft-ietf-ccamp-rsvp-te-sdh-otn-oam-ext
draft-ietf-ccamp-rsvp-te-mpls-tp-oam-ext
CCAMP WG
documents
Framework (1)
Ethernet OAM (2)
MPLS-TP OAM (4)
SDH and OTN OAM (3)
Recently adopted
WG documents

## Slide 4: Framework Updates
Scope is getting clarified
  P2p uni- and bidirectional end-to-end OAM configuration
    Discussion on segment OAM configuration in
  draft-kern-ccamp-intermediate-node-config-00 (tomorrow)
  P2mp?
Dedicated sub-TLV allocated for OAM Function Flags for extensibility
Path/Resv exchanges and OAM configuration steps detailed
  Establishment of OAM Entities and Functions
  Adjustment of OAM Parameters
  Deleting/removing OAM Entities and Functions

## Slide 5: Steps for OAM establishment Highlights only
Initiator
  Sets up OAM entities with source/sink functions but no OAM messages are emitted
  OAM alarms suppressed
  Path is sent with OAM Configuration information and cleared "OAM Alarms Enabled" ADMIN_STATUS bit
Remote-end receives Path message
  Configures OAM source/sink functions and in case of bidirectional connection starts sending OAM messages
  OAM alarms are suppressed
  Sends Resv message with adjusted OAM parameters if needed/allowed
Initiator receives Resv message
  Checks if OAM Configuration information is acceptable
  Finalizes OAM source/sink configuration and starts emitting OAM messages
  Refreshes connection with "OAM Alarms Enabled" ADMIN_STATUS bit set
Check details in draft-ietf-ccamp-oam-configuration-fwk!

## Slide 6: Next Steps
draft-ietf-ccamp-oam-configuration-fwk
  P2mp?
  Finalize IANA section
  WG LC
draft-ietf-ccamp-rsvp-te-eth-oam-ext
  Need to clean up text
draft-ietf-ccamp-rsvp-te-sdh-otn-oam-ext
  TCM and non-intrusive monitoring removed
  Need to clean up text
draft-ietf-ccamp-rsvp-te-mpls-tp-oam-ext
  Next…