## Slide 1: draft-ietf-ccamp-rsvp-te-mpls-tp-oam-ext-01 Configuration of pro-active MPLS-TP OAM functions using RSVP-TE or LSP Ping
Elisa Bellagamba Ericsson
Loa Andersson Ericsson
Pontus Sköldström Acreo
David Ward Juniper

## Slide 2: Overview
To specify the mechanisms necessary to establish MPLS-TP OAM entities monitoring an LSP and define information elements and procedures to configure pro-active MPLS OAM functions.
OBJECTIVE
Previous
Version
Configuration for BFD CC and CV
  Discriminators configuration
  Unique MEP ID configuration
  Symmetric timers configuration

## Slide 3: Changes respect to draft-bellagamba-ccamp-rsvp-te-mpls-tp-oam-ext-03 [1]
Aligned with draft-ietf-ccamp-oam-configuration-fwk and the others technology-specific configuration drafts
Adopted as Working Group document
Added the configuration for the following functionalities:
  Performance Monitoring Loss as specified in draft-frost-mpls-tp-loss-delay
  Performance Monitoring Delay as specified in draft-frost-mpls-tp-loss-delay
  Fault Management Signal as specified in draft-sfv-mpls-tp-fault
Several choices for timers configuration for BFD added:
  no configuration: negotiation entirely demanded to BFD
  symmetric configuration
  asymmetric configuration

## Slide 4: Changes respect to draft-bellagamba-ccamp-rsvp-te-mpls-tp-oam-ext-03 [2]
MPLS OAM configuration can be done via LSP-ping:
  the TLV structures originally defined for RSVP-TE can be entirely reused for LSP-ping
The “unique MEP-ID” field necessary for CV follows the specification in draft-swallow-mpls-tp-identifiers:
<"Unique MEP-ID of source of BFD packet"> ::= <src_node_id><src_tunnel_num><lsp_num>
While for LSP ping a new TLV has been defined, for RSVP-TE the necessary info can already be found in the following mandatory object:
src_tunnel_num  Tunnel ID [SESSION obj]
src_node_id  Tunnel Sender Address [SENDER_TEMPLATE]
LSP_Num  LSP ID [SENDER_TEMPLATE]

## Slide 5: Next Steps
Work in parallel with the work done in MPLS-TP
Receive more comments from the Working Group