## Slide 1: Framework for GMPLS and PCE Control of G.709 Optical Transport Networks
CCAMP WG, IETF 77th, Anaheim, California, USA
draft-zhang-ccamp-gmpls-g709-framework-02.txt
Fatai Zhang (zhangfatai@huawei.com)
Dan Li (danli@huawei.com)
Han Li (lihan@chinamobile.com)
Sergio Belotti (sergio.belotti@alcatel-lucent.it )

## Slide 2: Changes from 00
We welcome a new co-author (sergio.belotti@alcatel-lucent.it) and new contributors (Malcolm Betts, Pietro Grandi, Eve Varma); Thanks to Maarten Vissers.
Reconstructed Section 3, which is about OTN overview from the perspective of control plane.
Generalized two kinds of network topology from the perspective of control plane.
Removed non-normative stuff, e.g., ODU3ex.
Removed description of LO ODU terminology and two typical ODU connection examples to Appendix A.
Note that we had version 01, but it is not presented.

## Slide 3: Reconstruction on Section 3
Client Signal Mapping
ODU types and parameters
Multiplexing ODUj onto Links (i.e., TS allocation)
Link parameters
TPN (Tributary Port Number) Assignment

## Slide 4: Conn Management of the ODU (1)
ODU layer:
ODXC
Node A
ODXC
Node B
ODXC
Node C
ODXC
Node D
ODXC
Node E
Link #1
Link #2
Link #3
Link #5
Link #4
Work only with the ODU layer
In this layer there are links with a variety of TSes available, and nodes that are ODXCs (e.g., the ODU links (e.g., link#1-link#5) are presented between adjacent OTN nodes)
Lo ODU connections can be setup based on the network topology (e.g., Path computation will select a path that has the required number of TS available and offers the lowest cost. Signaling is then invoked to set up the path by carrying conn the information)

## Slide 5: Conn Management of the ODU (2)
ODU layer with OCh switching capability:
ODXC
Node A
ODXC
Node B
ODXC
Node C
ODXC
Node D
ODXC
Node E
Link #1
Link #2
Link #3
Link #5
Link #4
Node f
Node g
Node h
OTN nodes interconnect with wavelength switched node (e.g., ROADM,OXC) that are capable of OCh switching
It is MLN (i.e, ODU layer and OCh layer)
HO-ODU/OCh connection will appear at ODU level as a Forwarding Adjacency which will be used to create the ODU connection

## Slide 6: Next Steps
Adopt it as a WG document
Continue discussion with ITU-T
Comments are always appreciated