## Slide 1: GMPLS Signaling Extensions for the Evolving G.709 OTN Control
CCAMP WG, IETF 77th, Anaheim, California, USA
draft-zhang-ccamp-gmpls-evolving-g709-04.txt
Fatai Zhang <zhangfatai@huawei.com>
Guoying Zhang <zhangguoying@mail.ritt.com.cn>
Sergio Belotti <sergio.belotti@alcatel-lucent.it>
Daniele Ceccarelli <daniele.ceccarelli@ericsson.com>

## Slide 2: Changes from Version 03
Added a section to describe the extension to the Traffic Parameters to support ODUflex connection request
Removed non-normative things including ODU3e1 and ODU3e2

## Slide 3: Bandwidth of ODUflex(CBR)
( Bit Rate (BR), Bit Rate Tolerance (BRT) )
2.5Gbps * (1 - 50ppm) ~ 2.5Gbps * (1 + 50ppm)
The bandwidth of an ODUflex for CBR client signals can be represented as:
Where:
  BR = the nominal bandwidth of ODUflex
  BRT = the tolerance of ODUflex (up to 100ppm)
E.g., the actual bandwidth of an ODUflex with (2.5Gbps, 50ppm) is:

## Slide 4: Reservation of TS for ODUflex(CBR)
Total number of tributary slots on an OTUk link to be reserved for an ODUflex(CBR):
ODUflex(CBR) nominal Bit Rate×(1 + ODUflex(CBR) Bit Rate Tolerance)
ODTUk.ts Minimum Bit Rate
N = Ceiling of
Note: different ODUk links have different ODTUk.ts Bit Rate
Therefore, the total number of TS to be reserved for an ODUflex(CBR) on different links MAY NOT the same!
ODUk Minimum Nominal Maximum
(BR*(1-20ppm)) (BR*(1+20ppm))
ODU2 1.249 384 632 1.249 409 620 1.249 434 608
ODU3 1.254 678 635 1.254 703 729 1.254 728 823
ODU4 1.301 683 217 1.301 709 251 1.301 735 285

## Slide 5: Traffic Parameters Extension
ODUflex
ODUflex
A
B
C
(BR, BRT) = (2.5Gbps, +/-20ppm)
……
Therefore, (BR, BRT) information of an ODUflex (CBR) connection should be included in the signaling End-to-End
  Traffic Parameter is the most reasonable place to put the (BR, BRT)
2.5*(1-20ppm) / 1.302 = 2
Need 2 TSs
……
OTU4 link
Min. Bit Rate = 1.301 683 217Gps
OTU2 link
Min. Bit Rate = 1.249 384 632Gps
2.5*(1-20ppm) / 1.249 = 3
Need 3 TSs

## Slide 6: Traffic Parameters Extension
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Signal Type | Tolerance | NMC |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| NVC | Multiplier (MT) |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Bit_Rate |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

## Slide 7: Next Steps
Adopt it as a WG document
Refine it according to the feedback from the meeting or mailing list