## Slide 1: OSPF-TE extensions for GMPLS Control of Evolutive G.709 OTN
draft-ceccarelli-ccamp-gmpls-ospf-g709-01
CCAMP WG, IETF 77th Anaheim

## Slide 2: Agenda
OTN TE info needed for ODU path computation
  WSON TE info out of scope
Common interest to assure OSPF-TE routing extensions fully support OTN-G.709(2009) capabilities.
Requirements
  Detail of routing specific requirements from OTN FWK
Actual solution
  Being refined
Next Steps

## Slide 3: Requirements
Possibility of bundling links either at the same line rate or different line rates (e.g. 40G and 10G link total bandwidth)
  Bundling links at the same rate makes the calculation for ODU-flex routes slightly more precise while bundling links at different rates makes the control plane more scalable.
  The choice of the method is implementation dependent
Support priority for restoration.
  IETF requires supporting resource allocation at up to 8 priority levels.
Support any ODUs and ODU-flex
  Differently from other containers (that have a fixed size) it is needed to declare the maximum LSP bandwidth and the maximum number of LSPs that can be supported using this bandwidth.
  Concurrent path computation for ODUk and ODUflex
A
B
32 TS
24 TS
24 TS
Example: 3-odu3 – Max Band 32TS – Unres 80

## Slide 4: Requirements
Differentiate multiplexed capacity from line rate capacity
  Need not to lock connection service rate to infrastructure rate.
Perform accurate route calculation for containers that use a different number of time slot depending from the server rate.
  E.g. ODU2e

## Slide 5: Solution - 1
New ISCD
Max LSP Bandwidth and Unreserved bandwidth per priority
Flags for multiplexing capability declaration
1 ISCD per component links with same line rate and multiplexing capability
Drawbacks
  Bundling of component links with same OD(T)Uk and signal flags
  Concurrent path computation
    Example: 3-odu3 – Max Band 32TS – Unres 80
    How many service connections can be supported? 1 or 2?!?!
A
B
32 TS
24 TS
24 TS

## Slide 6: Next steps
Follow latest progresses on G.709
Progress the joint work aiming at finding a solution respecting all the requirements
New draft after the meeting

## Slide 7: QUESTIONS ?
THANK YOU