## Slide 1: LMP Test Messages Extensions for Evolutive OTN
draft-ceccarelli-ccamp-gmpls-g709-lmp-test-01
CCAMP WG, IETF 77th Anaheim

## Slide 2: Authors/Contributors
Daniele Ceccarelli
  daniele.ceccarelli@ericsson.com
Diego Caviglia
  diego.caviglia@ericsson.com
Francesco Fondelli
  francesco.fondelli@ericsson.com
Fatai Zhang
  zhangfatai@huawei.com
Dan Li
  danli@huawei.com
Marco Corsi
  marco.corsi@altran.it
Dieter Beller
  dieter.beller@alcatel-lucent.com

## Slide 3: Agenda
Link Connectivity Verification [RFC4204]
  Evolutive OTN needs LMP support to test new types of signal.
  BEGIN_VERIFY class
    Encoding Type
    Verify Transport Mechanism
    Transmission Rate
Trace Monitoring
  New TRACE object for evolutive OTN
  G.7714.1 Discovery Response msg for Layer Adjacency Discovery

## Slide 4: Link Connectivity Verification (1/2)
In band transmission of test messages over data link to verify physical connectivity, discover DP resources, exchanged IF_Id
Begin Verify Class: [RFC4204]

## Slide 5: Trace Monitoring (1/2)
Trace Object Class: [RFC 4207]
  New C-Type (2)
  Trace Type: Used to identify the type of trace message
    ODU TTI, OUT TTI and 6 levels of TCM

## Slide 6: Trace Monitoring (2/2)
Trace Object Class: [RFC 4207]
  New C-Type (2)
  Trace Length: Expresses the length of the trace message in bytes
  Trace Message:
    Includes the value of the expected message to be received in-band.
    The valid length and value combinations are determined by the ITU.T G.709 recommendation

## Slide 7: Discovery Response Message for Layer Adjacency Discovery
[G.7714.1] – Automatic layer adjacency discovery procedure applicable to G.709 OTN
  Discovery message sent via TTI
  Appendix III of G.7714.1 describes how to send a discovery response message to the originator (“discovery agent”) via LMP.
  TraceMonitor message [RFC4207] is used to convey the discovery response message.
  Discovery response message attributes mapping into TraceMonitor message objects or other fields of the LMP message

## Slide 8: Next steps
Keep on monitoring G.7714.1
Reflect OTN capabilities into
  LMP behavior negotiation ID
    OTN test bit in ENHANCED_BEHAVIOR_CONFIG (c-type=3)
  OTN control framework ID
Adopt as working group document

## Slide 9: QUESTIONS ?
THANK YOU