## Slide 1: RSVP Resource Sharing Remote Identification Association
draft-narayanan-tsvwg-rsvp-resource-sharing-02
Francois Le Faucheur
Ashok Narayanan
Subha Dhesikan
IETF 77

## Slide 2: History
narayanan-tsvwg-rsvp-resource-sharing-01
berger-ccamp-assoc-info-00
ASSOCIATION Object as defined in RFC 4872 and RFC 4873
Non-GMPLS “Resource Sharing” Association
Upstream Association
Extended Association ID
Resource Sharing Remote Identification Association
berger-ccamp-assoc-info-01
ASSOCIATION Object as defined in RFC 4872 and RFC 4873
Non-GMPLS “Resource Sharing” Association
Upstream Association
Extended Association ID
narayanan-tsvwg-rsvp-resource-sharing-02
Resource Sharing Remote Identification Association
IETF 76
IETF 77

## Slide 3: Summary
Extension to draft-berger-ccamp-assoc-info
Standards Track
defines a new association type called "Resource Sharing Remote Identification"

## Slide 4: Resource Sharing Remote Identification association
can be used by the sender to convey to the receiver information that can then be used by the receiver to identify an upstream initiated resource sharing
useful in upstream initiated resource sharing applications where the identification of the resource sharing association is not known a priori by the receiver, and instead is known by the sender
type-specific association rule:
  The Resource Sharing Remote Identification association does not create any association across Path states.

## Slide 5: Resource Sharing Remote Identification association
Sender
Receiver1
Cloud of RSVP Routers
Receiver2
Path (RSRID, ID=S/100)
Path (RSRIS, ID=S/100)
Resv (RS, ID=S/100)
Resv (RS, ID=S/100)
RSRID = “Resource Sharing Remote Identification” association
RS= “Resource Sharing” association
ID= Association Identification
Resource Sharing across the two reservations

## Slide 6: Next Step
Please review

## Slide 7: Backup Slides

## Slide 8: Recap of problem
Currently RSVP flows with different SESSION objects cannot share resources
There are some use cases where this is important
  Symmetric NAT
  VoIP call sharing
Proposed solution: separate resource sharing from SESSION object

## Slide 9: Problem: VoIP features
Sharing bandwidth between calls currently in call-waiting
Shared calls between shared-line extensions at different locations
Sharing not possible in RSVP for reservations going to different {L3,L4} destinations
A
B
C
Share?

## Slide 10: Problem: Symmetric NAT
Unidirectional flows to the same destination, traversing symmetric NAT
NAT issues different destination ports to the different senders
Sharing not possible in RSVP for reservations going to different {L3,L4} destinations
A
B
C
Share?
Symmetric NAT