## Slide 1: draft-sun-ccamp-dpm-01.txt
Label Switched Path (LSP) Data Path Delay Metric in Generalized MPLS/MPLS-TE Networks
The DPPM author team
Guoying Zhang
< zhangguoying@mail.ritt.com.cn>
draft-sun-ccamp-dpm-00
Notes: Subordinate draft of the DPPM draft

## Slide 2: Motivations
Work on the DPPM draft is now complete
  Now RFC 5814, a proposed standard
  It defines metrics and methodologies for control plane LSP delay, with the following assumptions
    Implementations are conformant with RSVP-TE specs
    Data paths are ready to forward traffic at respective signaling points [2]
    No errors occurs in cross-connect programming
For some reasons, implementations may be less than ideal [1]
  Pipelined cross-connect programming
  Difficult to get programming status
  Implementation deficiency
Purpose of the DMP draft
  To verify data path availability upon completion of signaling
  To measure delay, e.g., delay between completion of signaling and when data path is available
[1] draft-shiomoto-ccamp-switch-programming
draft-sun-ccamp-dpm-00

## Slide 3: Contents
Uses the same document framework as RFC5814
  Singleton
  Sample
  Statistics
  The only difference is that we define Sample in a general way, so no need to define Samples for different Singleton values separately
   reduced length, increased readability
Defines three data path related metrics
  RRFD: the delay from RESV Received to Forward data path becomes available
  RSRD: the delay from RESV Sent to Reversed data path becomes available
  PRFD: the delay from PATH Received to Forward data path becomes available

## Slide 4: Changes in the -01 revision
Incorporated some comments we received for the DPPM draft during the WGLC and IESG review process, mostly editorial
These include
  [A singleton metric is]Either a real number or an undefined number of milli-seconds.  [A singleton metric is] Either a real number of milli-seconds or undefined.
  Bi-directional  bidirectional
  Enriched Security Considerations section

## Slide 5: Change on the intended status
From standards track to informational
Reasons
  We used a general term “error free signal” for all possible data plane implementations
  No specific data plane technology is addressed in detail
  Thus more suitable for informational status
  And, we want to reduce the time to progress
One more reason
  We are considering composing another draft, for DPM measurement in the special case of packet capable interfaces
  May need to specify a “measurement protocol”
Notes: 测量报文格式（时标、序号的携带），以及测试的过程等。

## Slide 6: Next steps
We hope that the WG could take on it as a working item
Revise the draft according feedbacks from the WG
Solicit comments/suggestions on the necessity of composing a standard track draft for DPM on packet interfaces