## Slide 1: GMPLS RSVP-TE Recovery Extension for data plane initiated reversion and protection timer signalling draft-takacs-ccamp-revertive-ps-04.txt
Attila Takacs – Ericsson
Francesco Fondelli – Ericsson
Benoit Tremblay – Ericsson
IETF-77 Anaheim

## Slide 2: Background, Motivation and Objectives
Currently RSVP-TE extensions do not address the configuration of protection switching timers neither provide information on the protection switching operation mode (i.e., revertive or non- revertive)
  Hold-off time (HOFF) [RFC4427]
    Time between the reporting of signal fail or degrade, and the initialization of the recovery switching operation
  Wait-to-Restore time (WTR) [RFC4427]
    Time that must elapse after a recovered fault before an LSP can be used again to transport the normal traffic and/or to select the normal traffic from the LSP
  Reversion refers to the process of moving normal traffic back to the original working LSP after the failure is cleared and the path is repaired [RFC4427]
These parameters are important for recovery in any transport network
  GMPLS RSVP-TE signaling should be able to carry the necessary information
  Also required for MPLS-TP

## Slide 3: Proposal
Update Protection Object format (C-Type 2) allowing sub-TLVs
Eases future extensions of the Protection Object
0 1 2 3
  0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
  +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
  | Length | Class-Num(37) | C-Type(2 IANA)|
  +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
  |S|P|N|O| Reserved | LSP Flags | Reserved | Link Flags|
  +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
  |I|R| Reserved | Seg.Flags | Reserved |
  +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
  | |
  ~ sub-TLVs ~
  | |
  +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Introduce WTR and HOFF sub-TLVs

## Slide 4: Next steps
Identified in MPLS-TP Control Plane Framework as needed extension to fulfill TP requirements
  draft-abfb-mpls-tp-control-plane-framework-02
Adopt as WG document or progress the proposal together with other protection extensions