## Slide 1: Use Cases and Alternatives for Configuring Intermediate Nodes using RSVP-TE draft-kern-ccamp-intermediate-node-config-00 & Encoding of Attributes of LSP Intermediate Hops using RSVP-TE draft-kern-ccamp-rsvpte-hop-attributes-00
András Kern – Ericsson
Attila Takács – Ericsson
IETF-77 Anaheim

## Slide 2: Background, Motivation and Objectives
Multiple use-cases identified requiring specific configuration at intermediate nodes of an LSP
  OAM Configuration of Non-Intrusive Monitoring Entities
  OAM Configuration for Tandem Connection Monitoring
  WSON Regeneration, modulation type, FEC code changes
    draft-bernstein-ccamp-wson-signaling-06
  MPLS FRR
    draft-dong-ccamp-rsvp-te-plr-designation-00
LSP Attributes (RFC5420) primarily deals with attributes that are relevant to the whole LSP
Currently, it is not possible to declare and signal attributes to a specific intermediate hop of the LSP

## Slide 3: Discussion
Scalability issues raised in Hiroshima about adding a new “HOP_ATTRIBUTES” sub-object to the ERO to carry hop specified configuration
This document summarizes use cases and collects extension options
  Using the LSP_ATTRIBUTES Object
  Using the HOP_ATTRIBUTES Sub-Object in ERO
  Combination of LSP_ATTRIBUTES and ERO
  Using multiple messages
    Multiple messages with semantic fragmentation
    Using other signaling messages/procedures
Discussed
in Hiroshima

## Slide 4: Next Steps
Further discussion on alternatives…
  For intermediate node configuration two methods may be needed
  Support cases where path setup and intermediate node configuration need to be done congruently
    For simple configurations only
    Use the ERO with a new HOP_ATTRIBUTES Sub-Object
    draft-kern-ccamp-rsvpte-hop-attributes-00.txt
  For complex configurations we may need to rely on multiple message exchanges to scale
    Something along the lines of semantic fragmentation described for P2MP LSPs may be useful
Solicit feedback and comments from the WG
  Other use-cases?