## Slide 1: RSVP-TE Extensions to Realize Dynamic Binding of Associated Bidirectional LSP
MPLS/CCAMP WG, IETF 77th, Anaheim, US
draft-zhang-mpls-tp-rsvpte-ext-associated-lsp-00
Fei Zhang
Fan Yang
ZTE Corporation

## Slide 2: Problem Statements
Requirements (RFC5654/TP-CP-Framework)
  The end points of an associated bidirectional transport path MUST be aware of the pairing relationship of the forward and backward paths used to support the bidirectional service.
  Nodes on the path of an associated bidirectional transport path where both the forward and backward directions transit the same node in the same (sub)layer as the path SHOULD be aware of the pairing relationship of the forward and the backward directions of the transport path.

## Slide 3: Possible solutions
GMPLS calls (RFC4974) may serve as the foundation (TP-CP-Framework)
  Negotiate call ID (notify message)
Association object…
Two new defined Association Types
  Association (master/slave mode)
  Association (peer mode)
Tunnel Sender Address
Tunnel ID

## Slide 4: Association (master/slave mode)
trigger
LSP1/LSP2 already exist, bound together by Path refresh message
LSP1/LSP2 triggered at the same time, can not bind together
  (1) comparing the Router ID,
  (2)The bigger one sends Path refresh message, carrying the Association object of the reverse LSP
  (3) bound together

## Slide 5: Association (peer mode)
trigger
LSP1/LSP2 already exist, bound together by Path refresh message
LSP1/LSP2 triggered at the same time, do not need to send Path refresh message

## Slide 6: Association VS Call
 | Association | Call
The edge nodes | Support (Association object) | Support (Call ID)
The same transit nodes | Support (Association object) | Support (Call ID)
Association/connection setting up | Dependent (Path message) | Independent (Notify message)
Deleting the binding, not affect the LSPs | Support (by Path refresh) | Non Support (change the Session object)
Association between existing LSPs | Support (by Path refresh) | Non support (change the Session object)
Association object or GMPLS call ?
Using GMPLS calls to get call ID, then putting call ID into Association object?

## Slide 7: Next Steps
Solicit feedback and comments from the WG
Any comments are welcome 