## Slide 1: Requirements for auto-config of control plane adjacency draft-roch-ccamp-reqts-auto-adj-00.txt
IETF 77 – Anaheim – Mar’10
E. Roch (Ciena) eroch@ciena.com
T. Marcot (France Telecom) thierry.marcot@orange-ftgroup.com
L. Ong (Ciena) lyong@ciena.com

## Slide 2: Background
Control of dynamically signaled hierarchical LSPs
  Defined in draft-ietf-ccamp-lsp-hierarchy-bis-07.txt
  Approved and under A-D evaluation
Problem Statement
  Identifying additional requirements for applying this to multilayer control in ASON networks
  Submitted on behalf of OIF
  For evaluation by CCAMP
    Is this within CCAMP scope?
    Are protocol extensions needed to support these?

## Slide 3: Multilayer ASON Requirements
Client layer LSP established via LSP hierarchy
  Signaled information
    Higher layer interface id
    Action (advertised or not)
    Target IGP
    Bundle and component ids
    Status
ASON issues
  Need to support flexible client adaptation
    Multiple client layers may be supported by the server layer
  Need to support flexible control plane distribution
    data plane resource id vs. control plane entity id
    control plane routing entity id vs. signaling entity id
    control plane entity id vs. its control plane address

## Slide 4: Initial evaluation of current support
Per Layer Information | Current Support
Area ID | Y
Node ID | Y
Link ID | Y
Link Bundle ID | Y
Client Layer ID | N
Client Layer Signaling Controller ID | N
Client Layer Signaling Controller Address | N
Client Layer Routing Controller ID | N
Client Layer Routing Controller Address | N

## Slide 5: Next Steps
CCAMP to evaluate problem statement
  Any questions back to OIF or authors
  Evaluate if this is in scope for CCAMP
  Evaluate if extensions are needed to LSP Hierarchy
    e.g., additional TLVs in the LSP_Tunnel_Interface_ID object