## Slide 1: PLR Designation in RSVP-TE FRR
J. Dong, M. Chen, C. Liu
CCAMP, March 2010
draft-dong-ccamp-rsvp-te-plr-designation-00

## Slide 2
Ingress node can specify protection requirement for the protected LSP
  Using flags in SESSION ATTRIBUTE Object
    Local protection desired
    Label recording desired
    SE style desired
    Bandwidth protection desired
    Node protection desired
Specification of protection style is at the granularity of the whole LSP
  Not flexible
  Unnecessary cost
RFC 4090 FRR Review

## Slide 3: Problem Statement
All LSRs (except egress) must follow the PLR behavior
As many as (N-1) Backup LSPs
Do we need backup LSPs everywhere?
  Some nodes/links are reliable enough at LSP level
  Cost of Computing, Establishing & Maintaining backup LSPs
  Bandwidth reserved for backup LSPs
R4
R2
R3
R1
R5
R8
R6
R7
PLR
PLR
PLR
PLR
Primary LSP
Backup LSP

## Slide 4: Problem Statement (Cont.)
There can be requirement to specify protection style at the granularity of LSRs
  Operators can have more control on backup LSPs
  Not all LSRs need to behave as PLRs of the protected LSP
  Potential signaling and bandwidth savings
More flexible fast reroute signaling is needed
Protection Policy:
R2: link protection
R3: node protection
R1, R4: no protection required
R4
R2
R3
R1
R5
R7
R6
R8
PLR
PLR
Primary LSP
Backup LSP

## Slide 5
ERO IPv4/IPv6 Sub-objects Extension
  Use the reserved field in sub-objects as Flags
  IPv4 prefix sub-object
  IPv6 prefix sub-object
Proposed Solution

## Slide 6
Flag Definition
  P bit: Hop Local Protection flag
    0: local protection is determined by local protection flag in SESSION ATTRIBUTE Object
    1: local protection is not desired on this node
  N bit: Hop Node Protection flag
    0: protection style is determined by node protection flag in SESSION ATTRIBUTE Object
    1: node protection is desired on this node
Proposed Solution (Cont.)

## Slide 7
Backward Compatibility
  When new flags are set to 0, the behavior is the same as is
  Legacy LSR can not recognize the new flags, local protection is still based on existing flags in SESSION ATTRIBUTE Object
session local protection desired | session node protection desired | P bit | N bit | Hop Protection Style
0 | / | / | / | No Protection
1 | 0 | 0 | 0 | Link Protection
1 | 0 | 0 | 1 | Node Protection
1 | 0 | 1 | / | No Protection
1 | 1 | 0 | / | Node Protection
1 | 1 | 1 | / | No Protection
Proposed Solution (Cont.)

## Slide 8: Comments from mailing list
Why do we need to specify per-hop protection style?
  More flexible signaling for TE FRR
  Allow better control on backup LSPs
  Potential bandwidth and resource saving
RFC 4873 (GMPLS Segment Recovery) has similar effect
  This validates the requirement of PLR designation
  In packet switch network, we can use RFC 4090 or RFC 4873 for local protection, mostly will use RFC 4090
  This draft is a backward compatible enhancement to RFC 4090

## Slide 9
Collecting comments & feedbacks
Revise the draft
WG document?
Next Steps

## Slide 10: Thank You