## Slide 1: Signaling RSVP-TE P2MP LSPs in an Inter-domain Environment draft-ali-mpls-inter-domain-p2mp-rsvp-te-lsp-03.txt Zafar Ali, Cisco Systems N. Neate, Data Connection Ltd

## Slide 2: Requirements for inter-domain P2MP tree computation
End-to-end Path has to be remerged free (may also need to be cross-over free).
P2MP LSPs may need to be stitched at the border nodes, or hierarchical P2MP LSPs.
Loose hop expansion at the border node such that overall P2MP LSP is remerge free.
RFC4875 (RSVP-TE extensions for P2MP TE) does not address inter-domain requirements.
RFC5151 (inter-domain RSVP-TE extensions) does not address P2MP LSP setup.
RFC4920 does not address crankbacks for P2MP LSP.

## Slide 3
B19
C
S
D
B23
B22
B21
B1
B2
D2
B24
D1
H
B26
B20
B16
J
B15
B17
G
Issues with Loose ERO expansion for P2MP LSPs
B18
RSVP-TE signaling based solutions to address these requirements are not defined in RFC4875.
The above mentioned situation can even lead to infinite signaling loop!
ERO-L (D1)
ERO-L (D2)
Remerge happens at (C) in domain 3
Domain 1
Domain 2
Domain 3
Domain 4

## Slide 4: Solution
Ingress selects the same domain border node for ERO expansion for all siblings transiting a given domain. Domain border nodes expands EROs for all siblings S2L such that the overall path taken by these siblings in the domain is remerge free.
Crankback Signaling:
  Does not require selection of same domain border node for all siblings transiting a given domain.
  For siblings that have failed the LSP setup, on receipt of a PathErr a domain border node may hold the PathErr.
  The domain border node may try to signal an alternate path through the domain, for siblings that have failed the LSP setup.
  If a subsequent attempt is successful, the domain border node discards the held PathErr message.
  If all subsequent attempts are unsuccessful, the domain border node send a PathErr with a new cause to the Ingress node.
  Ingress node tries to find an alternate domain for the siblings failed the setup.

## Slide 5: Next Steps
We would like to request chairs of CCAMP and MPLS WG to decide where this work will belong.
We would like to make this document a WG Document.

## Slide 6
Thank You.