## Slide 1: RSVP Extension for Muti-Topology Support
Quintin Zhao, qzhao@huawei.com
Huaimo Chen, Huaimochen@huawei.com
Luyuang Fang, lufang@cisco.com
Chao Zhou, czhou@cisco.com
Lianyuan Li, lilianyuan@chinamobile.com
Xin Huang, huangxin@chinamobile.com
draft-zhao-rsvp-multi-topology-extension-00

## Slide 2: Background: IGP Support MT
IGP is extended to support Multi-Topology
  OSPF is extended to support Multi-Topology, RFC 4915
  ISIS is extended to support Multi-Topology, RFC 5120
Use MT-ID (a 12bit value) to identify logical topologies that overlay one physical topology
IGP (OSPF or IS-IS) computes separate SPF tree for each logical topology

## Slide 3: Extensions to RSVP-TE
Add MT Information into SESSION object
  Extended P2P SESSION object for IPv4
IPv4 Tunnel End Address
Extended Tunnel ID
Tunnel ID
MT-ID (12 bits)
Resv
Extended P2MP SESSION object for IPv4
P2MP ID
Extended Tunnel ID
Tunnel ID
MT-ID (12 bits)
Resv

## Slide 4: MPLS Forwarding in MT
Option 1: MT is implied by Label
  On a LSR, same FEC with different MT-ID are mapped to different Label
  Advantages: No changes on the forwarding plane
  Disadvantages: Label space is limited
Option 2: MT is indicated by stacked Label
  One extra label is stacked to indicate a topology
  Advantages: Each topology has a full label space
  Disadvantages: Forwarding is complicated

## Slide 5: Next Step:
Look for suggestions and comments;