## Slide 1: Signaling Extensions for Wavelength Switched Optical Networks
draft-bernstein-ccamp-wson-signaling-06.txt
Greg Bernstein Grotto Networking
Young Lee Huawei
Sugang Xu NICT
Hiroaki Harai NICT

## Slide 2: WSON Signaling Extensions
Provide extensions to Generalized Multi-Protocol Label Switching (GMPLS) signaling for control of Wavelength Switched Optical Networks (WSON).
Changes from 05:
Aligned with updated draft “draft-ietf-ccamp-rwa-wson-framework-05.txt” with inclusion of regenerators, OEO switches, and wavelength converters. This used to point to the “compatibility draft”.
Notes: <number>

## Slide 3: Signal Attributes and Processing
Modulation Type (TLV)
  Supports all ITU-T optical tributary classes
  Support for vendor specific modulation formats
FEC Type (TLV)
  Supports all ITU-T standard FECs
  Support for vendor specific FEC types
Regeneration Processing (TLV)
  Used to indicate that regeneration is to be performed on the signal at a particular node.
To be included as a subobject within an ERO or via some other mechanism. See Attila’s draft http://tools.ietf.org/html/draft-kern-ccamp-rsvpte-hop-attributes-00 )

## Slide 4: Next Steps
Adopt as a WG document 
Keep aligned with WSON framework, info and encoding drafts
Revise encodings as necessary
Notes: <number>