## Slide 1: Support for RSVP-TE in L3VPNs draft-kumaki-murai-ccamp-rsvp-te-l3vpn-02.txt
Kenji Kumaki KDDI Corporation
Tomoki Murai Furukawa Network Solution Corp.
Tomohiro Yamagata KDDI Corporation
Chikara Sasaki KDDI R&D Labs
March 2010
77th IETF@Anaheim
Notes: <number>

## Slide 2: Motivation
Service Providers will provide customer LSPs in BGP/MPLS VPNs.
  Requirements for RSVP-TE signaling for customer TE LSPs over BGP/MPLS VPNs are described.
    draft-ietf-l3vpn-e2e-rsvp-te-reqts-05 [RFC Ed Queue]
It is necessary that RSVP control messages, such as Path messages and Resv messages, are appropriately handled by PE routers.
Our goal is to establish an end-to-end MPLS TE LSP between customer sites.
77th IETF@Anaheim
March 2010
Notes: <number>

## Slide 3
Problem Statement
BGP/MPLS
IP-VPN
CE
CE
CE
CE
PE 1
VPN 1
VPN 1
VPN 2
VPN 2
VPN 2: MPLS TE LSPs
VPN 1: MPLS TE LSPs
PE 2
?
?
Path message
Resv message
The PE2 can’t identify Path messages between the VPN1 and the VPN2 when it sends them to the same destination.
The PE1 can’t identify Resv messages between the VPN1 and the VPN2 when it sends them to the same destination.
Need to extend from current specification (RFC 3209).
77th IETF@Anaheim
March 2010

## Slide 4: Object Definitions
Define the new object types
  LSP_TUNNEL_VPN-IPv4 / LSP_TUNNEL_VPN-IPv6 SESSION Object
  LSP_TUNNEL_VPN-IPv4 / LSP_TUNNEL_VPN-IPv6 SENDER_TEMPLATE Object
  LSP_TUNNEL_VPN-IPv4 / LSP_TUNNEL_VPN-IPv6 FILTER_SPEC Object
77th IETF@Anaheim
March 2010
Notes: <number>

## Slide 5: Object Definitions(cont.)
  LSP_TUNNEL_VPN-IPv4 / LSP_TUNNEL_VPN-IPv6 SESSION Object
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| |
+ +
| VPN-IPv4 tunnel end point address (12 bytes) |
+ +
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| MUST be zero | Tunnel ID |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Extended Tunnel ID |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
class = SESSION, LSP_TUNNEL_VPN-IPv4 C-Type = TBA
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| |
+ +
| VPN-IPv6 tunnel end point address |
// (24 bytes) //
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| MUST be zero | Tunnel ID |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| |
+ Extended Tunnel ID +
// (16 bytes) //
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Class = SESSION, LSP_TUNNEL_VPN-IPv6 C-Type = TBA
77th IETF@Anaheim
March 2010
Notes: <number>

## Slide 6
LSP_TUNNEL_VPN-IPv4 / LSP_TUNNEL_VPN-IPv6 SENDER_TEMPRATE Object
Object Definitions (cont.)
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| |
+ +
| VPN-IPv4 tunnel sender address (12 bytes) |
+ +
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| MUST be zero | LSP ID |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Class = SENDER_TEMPLATE, LSP_TUNNEL_VPN-IPv4 C-Type = TBA
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| |
+ +
| VPN-IPv6 tunnel sender address |
+ +
| (24 bytes) |
+ +
| |
+ +
| |
+ +
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| MUST be zero | LSP ID |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Class = SENDER_TEMPLATE, LSP_TUNNEL_VPN-IPv4 C-Type = TBA
77th IETF@Anaheim
March 2010

## Slide 7
Object Definitions (cont.)
LSP_TUNNEL_VPN-IPv4 / LSP_TUNNEL_VPN-IPv6 FILTER_SPEC Object
  Class = FILTER SPECIFICATION, LSP_TUNNEL_VPN-IPv4 C-Type = TBA
  Class = FILTER SPECIFICATION, LSP_TUNNEL_VPN-IPv6 C-Type = TBA
  * The format is identical to the LSP_TUNNEL_VPN-IPv4 / LSP_TUNNEL_VPN-IPv6 SENDER_TEMPLATE Object
77th IETF@Anaheim
March 2010

## Slide 8
Related drafts
Submit these drafts to PCE WG
  PCEP extensions for a BGP/MPLS IP-VPN
    draft-kumaki-murai-pce-pcep-extension-l3vpn-05
    PCC-PCE Communication Requirements for VPNs
    draft-ietf-pce-vpn-req-01
  BGP protocol extensions for Path Computation Element(PCE) Discovery in a BGP/MPLS IP-VPN
    draft-kumaki-pce-bgp-disco-attribute-06
77th IETF@Anaheim
March 2010

## Slide 9
Next Steps
Rename this I-D for l3vpn or mpls WG
Need more comments and feedback from WG
Request WG to accept this I-D as a WG document
77th IETF@Anaheim
March 2010
Notes: <number>