## Slide 1: mLDP Recursive FEC
Using mLDP through a Backbone where there is no Route to the Root
  draft-wijnands-mpls-mldp-recurs-fec
  Name changed from mldp-csc to better reflect focus
Has been presented to MPLS WG
  Also has a VPN component, so needs review by L3VPN WG
  Non-VPN part doesn’t seem controversial
  VPN part shouldn’t be controversial either 

## Slide 2: Functionality
How mLDP normally builds a MP LSP:
  Identifies MP LSP as <root, tunnel_id>
  LSP is built towards “root”
  All intermediate routers must have a route for “root”
So what about the familiar topology:
  R--P1---ASBR1---P2---ASBR2---P3---S
  where R wants to build a P2MP LSP to S, but
  P2 has no route to S

## Slide 3: Recursive FEC
  R---P1---ASBR1---P2---ASBR2---P3---S
R uses FEC <root=S, tunnel_id=Q>
ASBR1 changes FEC to:
  <root=ASBR2, tunnel_id=<S,Q>>
ASBR2 changes FEC to:
  <root=S, tunnel_id=Q>
Provides similar functionality as RFC 5496 (RPF Vector) provides for PIM
  Not exactly the same, as RPF vector is not part of tree identifier

## Slide 4: VPN with Inter-AS Option B
  PE1--P1---ASBR1---P2---ASBR2---P3---PE2
  ASBRs don’t have route to PE2
  ASBRs do have Intra-AS I-PMSI A-D route (non-segmented P-tunnels), NLRI is RD1:PE2
  P-tunnels need to follow A-D route path
  Recursive FEC needs to contain RD1
  For PIM/GRE tunnels, standard defines MVPN Join Attribute that extends RPF Vector so that PE1 can put RD in PIM Join
  For mLDP, need VPN Recursive FEC for same purpose

## Slide 5: VPN Recursive FEC
  PE1--P1---ASBR1---P2---ASBR2---P3---PE2
PE1 uses FEC <ASBR1, <PE2, RD, Q>>
ASBR find A-D route RD:PE2, ASBR2 is NH
ASBR1 changes to <ASBR2, <PE2, RD, Q>>
ASBR2 finds route to PE2
ASBR2 changes FEC to <PE2, Q>
Note that in the ASBR1/ASBR2 network, PE2 does not have to be a unique address, because RD is used in FEC

## Slide 6: Another Use of VPN Recursive FEC
  CE1--PE1---P1---PE2---CE2
Limited Applicability Carrier’s Carrier
  Only applies when 1-1 mLDP LSP mapping is desired
  CE1 uses FEC <CE2, Q>
  PE1 modifies FEC to <PE2, <CE2, RD, Q>>
  PE2 modifies back to <CE2,Q>
  Why is RD used? Only to ensure uniqueness of FEC in inner network.
Seems useful given applicability restrictions, when more complicated mechanisms are not needed

## Slide 7: Next Steps
MPLS WG will be asked to adopt as WG draft
L3VPN WG is asked to approve of the MPLS WG adopting it