## Slide 1: Time to Start New Work Items
  All WG drafts now on RFC Editor’s queue
  Those drafts have some known “holes” that need to be addressed
  There are a number of features not in the drafts that will be deployed over next several years
    Varying degrees of controversy, but
    Always best to have public specs that have been reviewed by WG
  Following slides propose specifics

## Slide 2: S-PMSI Join Extensions
Extensions needed for:
  IPv6 (C-S,C-G) flows
    Promised to IESG when base draft was approved
  MPLS P-tunnels
Very minor and straightforward extension of existing message from base draft
Covered in draft-rosen-l3vpn-mvpn-spmsi-joins, suggest adopting as WG draft

## Slide 3: Additional Miscellaneous IPv6 Clarifications
PIM/IPv6 inside GRE/IPv4 P-tunnel
  Covered in spmsi-join draft (perhaps not best place)
Other issues when C-PIM is v6, SP infra is v4:
  Option to configure use of separate P-tunnels for v4 and v6 C-flows?
  Encoding of PE addresses in BGP A-D routes (“originating PE” field) and RTs (GA field)
    Propose to encode as v4 addresses rather than v4-mapped v6 addresses
  New draft needed

## Slide 4: “Wild Card” S-PMSI Bindings
Very useful, multiple purposes:
  Use S-PMSI as default PMSI
  Assign customer shared tree to an S-PMSI
  Perhaps other ways of grouping flows (e.g., by C-S) and assigning to an S-PMSI
Covered in two very similar drafts:
  draft-rosen-l3vpn-mvpn-wildcards
  draft-rekhter-mvpn-wildcard-spmsi
  Proposal: produce joint draft for WG adoption

## Slide 5: Extranets
Wide agreement on need
Two existing drafts
  draft-rosen and draft-raggarwa, naturally
  Drafts complement each other through focus on different control planes
  Some differences in the extranet abstract model which need discussion
  draft-rosen contains some additional stuff (hub&spoke, anycast sources) that the WG might want to consider together or separately
Recommend collaboration on merged draft

## Slide 6: Bidirectional P-Tunnels
Mentioned a number of times in both base drafts
Complete spec not provided in those drafts
Folks differ on the merits of bidirectional tree technology, but:
  Technology is standard (e.g., RFC 5015, draft-ietf-mpls-ldp-p2mp)
  Should be included in MVPN toolkit
Covered in draft-rosen-l3vpn-mvpn-bidir
  Recommend adopting as WG doc
  Collaborators welcomed

## Slide 7: PIM/MS-PMSI
Topic of draft-rosen-l3vpn-mvpn-mspmsi
Specifies use of PE-PE PIM without:
  MI-PMSI
  Any P-tunnels that aren’t needed to carry data
Can be used with unidirectional (including segmented inter-AS) or bidirectional P-tunnels
Allows use of PIM control plane while significantly reducing core state and Hello overhead

## Slide 8: MS-PMSI
Given that the standard provides two control plane options, advances and efficiencies in each should be:
  supported,
  publicly specified
  reviewed by L3VPN WG
Recommend taking this work item and adopting the draft as WG draft.