## Slide 1: Proposal for Tuning IGMPv3/MLDv2 Protocol Behavior in Wireless and Mobile networks
draft-wu-multimob-igmp-mld-tuning-00
Qin Wu
Hui Liu

## Slide 2: Proposal for Tuning IGMPv3/MLDv2 Protocol Behavior in Wireless and Mobile networks
Objective
  Proposes a variety of optimization approaches for tuning
  IGMP/MLD protocols in wireless or mobile communication
  environment
Motivation
  Since IGMP/MLD are only designed for Shared Ethernet
  model [RFC1112], Specification for other types of network is
  required.
  Identify Impact of wireless and mobility on IGMP/MLD
  Evaluate current versions of IGMP and MLD
  Taking reliability, efficiency and different link type into account,
  tuning IGMP/MLD to adapt to the wireless environment.

## Slide 3: Impact of wireless and mobility on IGMP/MLD
The following characteristics when used in wireless and mobile networks are challenged
  ASM and SSM subscription ( REQ1)
  Fast Join and Leave (REQ2)
  Explicit Tracking (REQ3)
  Robustness to packet loss (REQ4)
  Minimum packet transmission (REQ5)
  Avoiding packet burst (REQ6)
  Adaptive to different link mode (REQ7)

## Slide 4: Evaluate current versions of IGMP and MLD
IGMPv2 [RFC2236] and MLDv1 [RFC2710] only support ASM communication mode, but not support SSM subscription and explicit tracking.
IGMPv3 [RFC3376] and MLDv2 [RFC3810] and their lightweight version LW-IGMPv3/LW-MLDv2 [RFC5760] support all the features of ASM and SSM communication, and of explicit tracking.
Current IGMPv3 and MLDv2 provide the reliability for these messages by unconditional retransmission like retransmission for startup query, last member query.
IGMPv3 and MLDv2 do not adopt host suppression mechanism, the number of active receivers on the network may occupy more bandwidth and influence the efficiency.
IGMPv3/MLDv2 and lightweight IGMPv3/MLDv2 are recommended as the best basis for optimization of IGMP/MLD to adapt to wireless and mobile networks

## Slide 5: IGMP/MLD Protocol tuning optimization approaches for Wireless or Mobile Network
Optimization Consideration for Report Messages
Optimization Considerations for Query Messages
  Disable Group/Source-Group Specific Queries on leave
  Limiting the scope of periodical Queries
  Conditional Retransmission of Queries on lost
  Unicast Query for retransmission of the lost solicited report
  Query Retransmission in incremental interval
Optimization Considerations for Link Type

## Slide 6: Optimization Consideration for Report Messages
Problem
  In some cases, the unsolicited reports are prone to loss due to network conditions degradation or long distance travel.
  Even the report can be retransmitted for [Robust Variable] times, the packet sent by the host is received by the router can not be guaranteed
  Excessive Packet retransmission is the waste of resource
Suggestions
Proposal 1 (Retransmission for unsolicited report)
  A host after sending an unsolcited report starts a retransmission timer and waits for the Acknowledgement (multiast data) from the router
  Upon receiving multicast data, the hosts stop retranmission
  If the multicast data is not received, unsolicit report can be retransmitted. A parameter should also be used to limit the maximum retransmission times for the report.
Proposal 2: (Ack for unsolicited report-Protocol change is required)
  A host after sending an unsolicited report starts a retransmission timer and waits for the acknowledgement (ACK) from the router.
  Upon receiving ACK or multicast data, the host stops the timer and retransmission.
  If the ACK is not received when the timer expires, another report is retransmitted.

## Slide 7: Optimization Considerations for Query Messages (1)
Disable Group/Source-Group Specific Queries on leave
  Suggestions(Explicit tracking+ Disable Group Queries on leave)
    Explicit Tracking can be used to keep track of the membership status of the hosts
    If Explicit Tracking is used, Group/Source-Group Specific Queries on leave is not necessary

## Slide 8: Optimization Considerations for Query Messages (2)
Limiting the scope of periodical Queries
  Problem
    Reduce the packet burst on link with large number of responded reports
  Suggestions (Periodical Query+Group Periodical Query)
    If the receiver number is small, the periodical General Queries for all multicast receivers can be used.
    If the number of the multicast receiver on a link is large, the router could choose to periodically send Group Queries to a (*,G) group in different time interval
    or send Source-Group Specific Queries to a (S,G) group in different time interval.

## Slide 9: Optimization Considerations for Query Messages (3)
Conditional Retransmission of Queries on lost
  Problem
    The router if after sending a Query, fails to get any response from any receiver, it may derive that its previous-sent Query might have been lost before reaching the receiver.
  Suggestions (Periodical Query + Conditional Query Retransmission)
    Conditional retransmission of Query may be adopted
    Only Query lost is detected, Query will be resent.
    Query is resent in the incremental interval in case of network congestion

## Slide 10: Optimization Considerations for Query Messages (4)
Unicast Query for the lost solicited report
  Problem
    A router after sending a periodical Query collects successfully all the members’ report responses except for one or two which are currently still valid in its database
  Suggestions (Periodical Query+ Unicast Query)
    Unicast a Query respectively to each non-respondent receiver to check whether they are still alive for the multicast reception, without affecting the majority of receivers that have already responded.
    Unicast query can be retransmitted in the incremental interval

## Slide 11: Optimization Considerations for Query Messages (5)
Query Retransmission in incremental interval
  Problem
    when a router can not collect successfully all the member’s report response and network congestion is going to happen
  Suggestions (Explicit tracking/Periodical Query+ Query retransmission in incremental interval)
    Query Retransmission can be slowed down
    The router stop Query when receiving report response from the host
    The router resend Query in the increment interval (e.g., double interval) at the each time of retransmission
    stops the sending of the Query when retransmission up-limit is reached.

## Slide 12: Optimization Considerations for Link Type
Delay Response which is used to prevent bursting of solicited reports, should not be required in PTP and PTMP link
  There is only one receiver in the link for each interface
  Without Delayed Response, the report could be responded
  to the router immediately
Group specific Query and Source-and-Group Specific Query, which are used to query other valid members, are not necessary for PTP and PTMP link
  There should be only one receiver on each link reporting toward the router
For PTP links, periodical General Query, which is sent separately to each interface, is unnecessary to be sent to all the interfaces
  Only the hosts which have made the group join and have reception state on the router are interested in the this periodical General Query

## Slide 13: Moving forward
Solicit more review and quick Feedback
Accept it as WG item?