## Slide 1: Fast Handover for Multicast in Proxy Mobile IPv6
draft-hui-multimob-fast-handover-00

## Slide 2: Abstract
This document specifies the fast handover mechanism to solve the problem of handover latency and packet loss in PMIP6.
Necessary extensions are specified for Handover Initiate (HI) and Handover Acknowledgement (HAck) messages to support multicast handover procedure.

## Slide 3: Problem Status
IP multicast is not well considered in fast handover for PMIPv6
  Only after the bi-directional tunnel is built between n-MAG and LMA using extended PBU (PBU-M) message, the multicast packet can be continuously delivered to MN.
  It inevitably causes the latency and loss of packet during handover process.

## Slide 4: Protocol Operation
Reference network for fast handover
  multicast tunnel is established to transfer the multicast data from p-MAG to n-MAG before the n-MAG joins the multicast group
  so that whenever the MN handovers to the n-MAG, it can receive the multicast data from n-MAG.

## Slide 5: Fast handover for PMIPv6 multicast
The p-MAG sends the HI to the n-MAG. The HI message includes MN ID and MN Multicast State.
The n-MAG sends the HAck back to the p-MAG.
The n-MAG requests the p-MAG to forward multicast packets by setting F flags in the HI message.
A tunnel is established between the p-MAG and n-MAG and multicast packets destined for the MN are forwarded from the p-MAG to the n-MAG over this tunnel.
The n-MAG starts to forward multicast packets destined for the MN after the handover.

## Slide 6: Message Format
HI Mobility Header message with multicast extension
  A new flag (M) is included in the HI Mobility Header message with multicast extension.
  The mobility options field needs to be extended to include the multicast addresses.

## Slide 7: Thanks