## Slide 1: Juan Carlos Zúñiga Guang Lu Akbar Rahman IETF 77, March 2010 http://www.ietf.org/id/draft-zuniga-multimob-smspmip-02.txt
Using Dedicated Multicast LMA

## Slide 2
Summary of Updates from IETF 76
Two updates were submitted to address comments from IETF 76 and mailing lists:
  First, the draft now concentrates on a dedicated Multicast LMA (LMA-M) as the main proposal, and other enhancements are removed
  Second, more details were added to show the protocol operation of the LMA-M
  Finally, an initial traffic analysis was done to show the benefits of the LMA-M in terms of minimization of packet replication

## Slide 3: Architecture of Dedicated Multicast LMA (LMA-M)
Multicast Services
Unicast Services
P-MAG
N-MAG
LMA-U
LMA-M
MN
MN
MN
Multicast Anchor
Unicast Anchor
MLD Proxy

## Slide 4: Protocol Operation Using Dedicated Multicast LMA (LMA-M)
P-MAG
N-MAG
LMA-U
LMA-M
MN
Multicast Traffic
Rtr Sol/Rtr Adv
MN Attaches to n-MAG
MN Detaches
Multicast Traffic
Multicast Tunnel
MLD Query/MLD Report (G)
Aggregated MLD Report (G)

## Slide 5: Advantages
Simplifies the multicast tree topology
  allows a PMIPv6 domain to closely follow a simple multicast tree topology for Proxy MLD forwarding
  Eliminates tunnel convergence issue at the MAG
  Minimizes the replication of multicast traffic when MNs with different LMAs join the same multicast group
Not all LMAs need multicast capability and connectivity
  Reduces total resources and states at LMAs

## Slide 6: 1 Million MNs Subscribed to Distinct Multicast Groups
PMIP Multicast Scheme | Redundant streams at MAG | Simultaneous streams at each LMA/LMA-M | Simultaneous streams in ntwk for all LMAs
Baseline Unicast/ Multicast LMA | 0 | 250,000 | 1,000, 000
Dedicated Multicast LMA | 0 | 1,000,000 | 1,000, 000
No redundant streams at MAG for both schemes
Single anchor LMA-M handles all streams
Overall number of streams in network is the same for both schemes

## Slide 7: 1 Million MNs Subscribed to Same Multicast Group
PMIP Multicast Scheme | Redundant streams at MAG | Simultaneous streams at each LMA/LMA-M | Simultaneous streams in ntwk for all LMAs
Baseline Unicast/ Multicast LMA | 3 | 200 | 800
Dedicated Multicast LMA | 0 | 200 | 200
LMA-M architecture reduces redundant traffic and therefore traffic load in the network
Only LMA-M has no redundant streams at MAG

## Slide 8: MNs belong to the Same Multicast Group – Using Combined LMA
LMA 1
LMA 2
LMA 3
LMA 4
MAG1
MAG 50
MAG 51
MAG 100
MAG 101
MAG 150
MAG 151
MAG 200
MN 250001-500000
MN 500001-750000
MN 750001-1000000
1 multicast group
1 Stream
1 Stream
1 Stream
1 Stream
# of simultaneous streams in network = 800
MN 1-250000

## Slide 9: MNs belong to the Same Multicast Group – Using LMA-M
MAG1
MAG 50
MAG 51
MAG 100
MAG 101
MAG 150
MAG 151
MAG 200
LMA -M
1 Stream
1 multicast group
LMA 1-U
LMA 1-U
LMA 1-U
LMA 1-U
MN 250001-500000
MN 500001-750000
MN 750001-1000000
MN 1-250000
# of simultaneous streams in network = 200

## Slide 10: Conclusions
As described, the dedicated Multicast LMA (LMA-M) architecture simplifies deployment and reduces redundant traffic load in the network
We will generate updated draft shortly with more details

## Slide 11
THANK YOU