## Slide 1: Tuning the Behavior of IGMP and MLD for Mobile Hosts and Routers
draft‐asaeda‐multimob‐igmp‐mld‐optimization‐02
Hitoshi Asaeda (Keio University)
Stig Venaas (Cisco)
77th IETF, March 2010, Anaheim, CA, USA
<number>

## Slide 2: Overview
Concept
  Minimize mobile node’s power consumption, and maximize the available wireless resource
  Save node and wireless link resources by limiting the number of transmitted IGMP/MLD messages while no additional join and leave latency is introduced
Approach
  Tune several IGMP/MLD timer values
  Configure router behavior based on the standard (RFC3376, 3810) functions
  No protocol change introduced
<number>
77th IETF, March 2010
Notes: <number>

## Slide 3: Changes from -01
Change the document title
  “Tuning the Behavior of IGMP and MLD for Mobile Hosts and Routers”
Move some functions to an extension draft
  Explicit membership notification
  Specific timer value for unicast general query
  Note: Extension draft
    draft-asaeda-multimob-igmp-mld-mobility-extensions-04
Describe potential values tuned
  Query interval, Query response interval, Startup query interval
  Robustness variable
<number>
77th IETF, March 2010

## Slide 4: Tracking of Membership Status
Enabling explicit tracking function on routers attached to MNs
  Longer general query interval will reduce the number of transmitted IGMP/MLD messages
Note
  Require router’s processing capacity and large memory
  Explicit tracking does not work properly in some case (e.g. non-upgraded hosts attached)
  Explicit tracking does not remove query-response communication
    Shorter general query interval will keep membership information consistent
77th IETF, March 2010
<number>
Notes: <number>

## Slide 5: Query Processing
Unicast general query
  Query can be transmitted to any address (RFC3376, 3810)
    All hosts addresses (224.0.0.1 and ff02::1) are used as the destination of general query in general
  Unicasting general query would be advantageous in some condition
    Need to analysis the “condition”
Group- and Group-and-source specific queries
  Destination address should be the corresponding multicast address to make only subscribers respond
77th IETF, March 2010
<number>

## Slide 6: Timers, Counters, Default Values
[Query Interval]
  Default: 125 sec.
  Larger values cause IGMP Queries to be sent less often
[Query Response Interval]
  Default: 10 sec.
  Larger values make the traffic less bursty
[Startup Query Interval]
  Default: 1/4 of [Query Interval]
  Shorter value such as 1 sec. contributes to slightly smooth handover (e.g. for PMIPv6)
[Robustness Variable]
  Default: 2
  Should not be bigger than 2, especially when [Query Response Interval] is set smaller than its default value
77th IETF, March 2010
<number>

## Slide 7: Next Step
More study of tuning values and considerations based on simulation result
Describe more wireless link specific issues
Comments are welcome
Adopt this draft as a WG document ?
77th IETF, March 2010
<number>

## Slide 8: IGMP/MLD Protocol Extension
draft-asaeda-multimob-igmp-mld-mobility-extensions-04
New functions
  Explicit membership notification (host-side only)
    Periodically notify membership status with Current state record
  IGMP/MLD Hold and Release (host- and router-side)
    Suspend-and-resume forwarding data
      Quick retransmission after handover
      Reduction of unneeded tree re-construction
New timers
  Unicast and multicast general query interval (router-side only)
    These timers may be dynamically changed
  Notification interval
  Hold interval
77th IETF, March 2010
<number>

## Slide 9: PMIPv6 Protocol Extension
draft-asaeda-multimob-pmip6-extension-03
Supported functions
  Local routing
  MAG with either PIM-SM or MLD proxy, or dual-mode (i.e. both PIM-SM and MLD proxy)
  Context transfer during handover
New function (for traffic aggregation)
  M-Tunnel: multicast dedicated bi-directional tunnel between LMA and MAG
New messages (for handover)
  PBU-M: PBU with multicast extension
  M-CTD: Multicast context transfer data for CXTP
77th IETF, March 2010
<number>

## Slide 10: Summary
IGMP/MLD protocol tuning
  draft-asaeda-multimob-igmp-mld-optimization-02
  Moving forward as a WG document ?
IGMP/MLD protocol extension
  draft-asaeda-multimob-igmp-mld-mobility-extensions-04
PMIPv6 protocol extension for mobility
  draft-asaeda-multimob-pmip6-extension-03
77th IETF, March 2010
<number>