## Slide 1: Base Deployment for Multicast Listener Support in PMIPv6 Domains draft-ietf-multimob-pmipv6-base-solution-00
Thomas C. Schmidt
t.schmidt@ieee.org
HAW Hamburg

## Slide 2: Status of the Draft
Previous version: draft-schmidt-multimob-pmipv6-mcast- deployment
  Presented in Hiroshima
  Has undergone extensive reviews and discussions
  WG adoption: Feb. ‘10
Defines a basic deployment for multicast support in PMIPv6 domains

## Slide 3: The PMIP Picture
+----+ +----+
|LMA1| |LMA2|
+----+ +----+
LMAA1 -> | | <-- LMAA2
| |
\\ //\\
\\ // \\
\\ // \\
+---\\------------- //------\\----+
( \\ IPv4/IPv6 // \\ )
( \\ Network // \\ )
+------\\--------//------------\\-+
\\ // \\
\\ // \\
\\ // \\
Proxy-CoA1--> | | <-- Proxy-CoA2
+----+ +----+
|MAG1|-----{MN2} |MAG2|
+----+ | +----+
| | |
MN-HNP1 --> | MN-HNP2 | <-- MN-HNP3, MN-HNP4
{MN1} {MN3}

## Slide 4: Multicast Deployment on PMIP
+-------------+
| Multicast |
| Source |
+-------------+
/ \
+----+ +----+
|LMA1| |LMA2| Multicast Anchor
+----+ +----+
LMAA1 | | LMAA2
| |
\\ //\\
\\ // \\
\\ // \\ Unicast Tunnel
\\ // \\
\\ // \\
\\ // \\
Proxy-CoA1 || || Proxy-CoA2
+----+ +----+
|MAG1| |MAG2| MLD Proxy
+----+ +----+
| | |
MN-HNP1 | | MN-HNP2 | MN-HNP3
MN1 MN2 MN3
Put Standard Mcast
Querier onto LMA:
DR or MLD Proxy
Put Standard MLD
Proxy onto MAG:
1 Instance per Uplink

## Slide 5: Combined Signaling: MCast on PMIP
MN1 MAG1 MN2 MAG2 LMA
| | | | |
| Join(G) | | | |
+--------------->| | | |
| | Join(G) | | |
| |<---------------+ | |
| | | | |
| | Aggregated Join(G) | |
| +================================================>|
| | | | |
| | Mcast Data | | |
| |<================================================+
| | | | |
| Mcast Data | Mcast Data | | |
|<---------------+--------------->| | |
| | | | |
| | < Movement to MAG2 & PMIP Binding Update > |
| | | | |

## Slide 6: Combined Signaling: MCast on PMIP (2)
MN1 MAG1 MN2 MAG2 LMA
| | | | |
| | < Movement to MAG2 & PMIP Binding Update > |
| | | | |
| | |--- Rtr Sol -->| |
| | | | |
| | | MLD Query | |
| | |<--------------+ |
| | | | |
| | | Join(G) | |
| | +-------------->| |
| | | Aggregated Join(G)
| | | +===============>|
| | | | |
| | Mcast Data | | |
| |<================================================+
| | | | Mcast Data |
| | | |<===============+
| Mcast Data | | | |
|<---------------+ | Mcast Data | |
| | |<--------------+ |
| | | | |

## Slide 7: Operations at Node Arrival
MAG-MN link comes up and MAG discovers MN
Unicast address configuration & PMIP binding  MAG can identify corresponding LMA
MAG SHOULD send MLD General Query to new downstream link (standard querier behaviour)
MAG SHOULD check MN’s multicast admissibility (a repeated answer may already configure the proxy interface state later)

## Slide 8: Operations at Node Arrival (cont‘d)
MAG adds new downstream link to MLD proxy instance uplinked to corresponding LMA
Proxy instance triggers an MLD General Query on its new downstream link (to be safe)
MLD Membership Report arrives at proxy (either answer)
Proxy instance updates states and reports upstream if needed

## Slide 9: Capabilities needed at Proxy
Automatic initial querying
Simultaneous support of MLD + IGMP
Configurable list of downstream interfaces that may be altered during runtime
Multiple instantiation with isolated forwarding on separated interfaces

## Slide 10: State of Proxy Implementations
All functions are around – but we did not see them combined in one implementation
Currently, we picked up Linux ecmh and started to extend
Collaborators Welcome!

## Slide 11: Summary & Outcome
Traffic flows/aggregation may be optimal, but need not be (see presentation on optimization)
Draft will be revised soon:
  Response to earlier reviews
  PMIPv6 Multihoming considerations to be added
  Security section to be revised
Questions:
  Are there other open issues / aspects to add ?
Proposal to WG:
Finish core work with upcoming revision

## Slide 12
Questions?