## Slide 1: LMP Behavior Negotiation
CCAMP WG, IETF 78th, Maastricht, Netherlands
draft-li-ccamp-lmp-behavior-negotiation-01.txt
Dan Li (danli@huawei.com)
D. Ceccarelli (daniele.ceccarelli@ericsson.com)
New Author Added!

## Slide 2: Problem Statement
New LMP behaviors and protocol extensions are being introduced
  RFC 4204: Basic LMP Messages (Msg Type 1-20)
  RFC 4207: TRACE behavior for SDH/SONET (Msg Type 21-31)
  RFC 4209: DWDM behavior (C-type 2 in CONFIG Object)
  RFC 5818: Data Channel Consistency Check behavior (Msg Type 32-34)
  Draft-ceccarelli-ccamp-gmpls-g709-lmp-test: Trace behavior for evolutive OTN (C-type TBA in TRACE Object)
Unfortunately, no procedure to discover the LMP capabilities of peer LSRs is defined so far
Reference Updated!

## Slide 3: Enhanced Behavior Config
Config Message (Msg Type = 1)
<Config Message> ::= <Common Header> <LOCAL_CCID> <MESSAGE_ID>
<LOCAL_NODE_ID> <CONFIG>
CONFIG Class = 6
o C-Type = 1, HelloConfig, defined in [RFC4204]
o C-Type = 2, LMP_WDM_CONFIG, defined in [RFC4209]
o C-Type = 3, ENHANCED_BEHAVIOR_CONFIG Newly defined!

## Slide 4: New C-Type (3) for CONFIG Object
The format of the new type of CONFIG Class is defined as follows:
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Reserved |M|O|W|S| Reserved |D|T|F|V|
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|<----- Architecture Flags ---->|<----- Capability Flags ----->|
Architecture Flags:
M – MPLS-TP; O – OTN; W – WDM; S – SONET/SDH
Capability Flags:
D – RFC 5818; T – Trace Monitoring; F – Fault Management; V – Verification;
Note: The Reserved field MUST be sent as zero and MUST NOT be ignored on receipt. This allows the detection of supported/unsupported LMP behaviors.
Format Changed!

## Slide 5: Next Steps
Adopt as a WG document
  Very simple draft
Update with LMP extensions of G.709 (OTN) control
  draft-ceccarelli-ccamp-gmpls-g709-lmp-test-02.txt
Comments?