## Slide 1: RFC 5787bis draft-malis-ccamp-rfc5787bis-00.txt
IETF 78 – Maastricht – Jul’10
L. Ong (Ciena) lyong@ciena.com on behalf of
Andy Malis (andrew.g.malis@verizon.com)
Acee Lindem (acee.lindem@ericsson.com)

## Slide 2: Main Changes
Objective: move ASON extensions from Experimental to Standards Track
  Reflecting experience gained from implementation and interoperability testing
Terminology and IANA section changes due to shift from Experimental to Standards Track
Prefixes Section
  Sections reorganized to explain terminology before defining prefix extensions (clarity)
  Prefix format change to reference RFC 5786 rather than defining a separate format
  Procedural change to allow advertisement of multiple Node Attribute TLVs when router supports multiple TE Router IDs

## Slide 3: Routing Information Advertisement
Within an RC, each level of supported RA represented as an OSPF instance
Import/Export Rules govern advertisement upward or downward in the RA hierachy
Greatly simplified from RFC 5787
  Election of RA to advertise information has been removed. It was flawed from the beginning. If required, a mechanism that works could be added in subsequent work.
  Misinformation regarding OSPF flooding removed
  Section on reconfiguration removed.
Notes: LFA network analyser tool
2010-07-12
<number>

## Slide 4: Inter-RA Loop Prevention
Must prevent routing information advertised upward or downward in the RA hierarchy is not readvertised into an RA from which is was advertised.
  For routing information advertised downward, must simply assure that routing information is never advertised upward since an RA at level N is fully contained by an RA at level N+1.
  For routing information advertised upward, one must assure that it is not advertised downward into the RA from which is was received. Since an RA at level N may fully contain multiple RAs at level N-1, checking the originating RA is necessary.
Notes: LFA network analyser tool
2010-07-12
<number>

## Slide 5: Inter-RA Loop Prevention - Continued
Two new Sub-TLVs to be included in the Router Advertisement TLV, Link-TLV, and Node Attribute TLV
  Inter-RA Export Upward Sub-TLV – Includes advertising RA ID for comparison when exporting downward.
  Inter-RA Export Downward Sub-TLV – Advertising RA ID for not needed for loop prevention – included for debugging purposes
New Sub-TLVs must be retained with the routing information for comparison when exporting information upward or downward based on policy
Notes: LFA network analyser tool
2010-07-12
<number>

## Slide 6: Open Question
Section 5.1 on identifiers
  Pi is the data plane entity
  Li is the control plane representation of Pi
  Ri is its associated control plane router
Somewhat unclear what is put into Router Address TLV
  Esp. Ri vs. Li - text mentions both
  Ri provides the routing function, Li may not participate in control plane
Pi
Li
Ri
Li