## Slide 1: Requirements for auto-config of control plane adjacency draft-roch-ccamp-reqts-auto-adj-01.txt
IETF 78 – Maastricht – Jul’10
E. Roch (Ciena) eroch@ciena.com
T. Marcot (France Telecom) thierry.marcot@orange-ftgroup.com
L. Ong (Ciena) lyong@ciena.com

## Slide 2: Background
Control of dynamically signaled hierarchical LSPs
  Requirements presented at IETF77
  Support for multiple client layers and address separation
  Extensions to draft-ietf-ccamp-lsp-hierarchy-bis-08.txt
Protocol Extensions
  Allows for multiple LSP_INTERFACE_ID
    One per layer
  Supports additional sub-TLVs
    For address separation

## Slide 3: Combining LSP_INTERFACE_IDs
C-NUM=193, C-Type = TBD
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| |
~ CLIENT_1_LSP_TUNNEL_INTERFACE_ID TLV ~
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| |
~ ... ~
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| |
~ CLIENT_N_LSP_TUNNEL_INTERFACE_ID TLV ~
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
}
Insert a sub-TLV for each client layer supported
Create a new LSP_INTERFACE_ID that allows multiple entries

## Slide 4: Identifying the layer
Each CLIENT_LSP_TUNNEL_INTERFACE_ID TVL has the following format.
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Length | Reserved | Type |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Encoding Type | Switching Type| Signal Type | Reserved |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| LSP_TUNNEL_INTERFACE_ID TLV (without header) |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
}
Layer Id
}
Type is C-Type corresponding to format of

## Slide 5: New Sub-TLVs for address Separation
Type 3 (TBD) RC PC ID
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Routing Controller Protocol Controller Identifier |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Type 4 (TBD) RC PC IPv4 Address
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Routing Controller Protocol Controller Reachable IPv4 Address |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Type 5 (TBD) SC PC ID
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Signaling Controller Protocol Controller Identifier |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Type 6 (TBD) SC PC IPv4 Address
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|Signaling Controller Protocol Controller Reachable IPv4 Address|
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+