## Slide 1: SONET/SDH BW draft-ong-gmpls-ason-routing-exper-02.txt
IETF 78 – Maastricht – Jul’10
L. Ong (Ciena) lyong@ciena.com
Andy Malis (andrew.g.malis@verizon.com)
Remi Theillaud (remi.theillaud@marben-products.com)
+ 7 other people who don’t “get” the ISCD

## Slide 2: Changes
Most proposals regarding RFC 5787 now in draft-malis-ccamp-rfc5787bis-00.txt
Remaining issue is optimization of SONET/SDH bandwidth advertisement
Separated out and attempting to develop common solution with OTN advertisement (also TDM) as requested

## Slide 3: Basic Idea
ISCD identifies switching capability, encoding type supported
RFC 4202/3 and RFC 5787 suggest using multiple ISCDs to advertise for different SONET/SDH signal types
  This is a lot of overhead and duplicate information
    Particularly if the TDM network does not support eight levels of priority – priority is not specified as a feature of ASON
  This relies on “min. reservable bandwidth” to distinguish one ISCD from another (since SC and encoding type are the same)

## Slide 4: Alternative
Advertise one ISCD for the smallest size signal type
  Still provides a high level bandwidth estimate in a generic format
Supplement with a TDM-specific object to carry more detail
  Bandwidth per signal type
  Only carries those priority levels supported (or no priority)
  More compact and easily interpreted for TDM