## Slide 1: Framework for GMPLS and PCE Control of G.709 Optical Transport Networks
CCAMP WG, IETF 78th, Maastricht, Netherlands
draft-ietf-ccamp-gmpls-g709-framework-02.txt
Fatai Zhang (zhangfatai@huawei.com)
Dan Li (danli@huawei.com)
Han Li (lihan@chinamobile.com)
Sergio Belotti (sergio.belotti@alcatel-lucent.it )

## Slide 2: Contents of this Draft
Informative overview of the OTN layer network
Connection management in OTN
GMPLS and PCE implications
  Hierarchy LSP in OTN
  GMPLS Signaling extension requirements
  GMPLS Routing extension requirements
  GMPLS LMP extension requirements
  PCEP requirements

## Slide 3: Changes from Version 00 & 01
Added some descriptions to indicate that "No additional Switching Type and LSP Encoding Type are required". (We can just reuse OTN LSP Encoding Type & Switching Type defined in RFC4328)
Refined the routing requirements
Added some text to refine ODU layer Hierarchy LSP
Added some text to reflect requirement to support operator policies re transporting ODU connection services (i.e., flexibility re usage of full lambda, or sub-lambda, capacity in network)

## Slide 4: Switching Type & Enc. Type
LSP Encoding Type and Switching Type are consistent with [RFC4328]
  Switching Type :
    G.709 ODUk (Digital Path) ---> TDM
    G.709 Optical Channel (OCh) ---> LSC
  LSP Encoding Type:
    12 ---> G.709 ODUk (Digital Path)
    13 ---> G.709 Optical Channel (OCh)
Note:
  ODU0/ODU1/ODU2/ODU2e/ODU3/ODU4/ODUflex/… belong to the same encoding type and switching type, They just have different switching granularities
Infinite number of switching granularities
-> one single tech layer from CP perspective

## Slide 5: OTN Routing Requirements
The following requirements should be considered for OTN routing:
  Support for carrying the link multiplexing capability
    Indicate which LO ODUj can be multiplexed into the ODU switching capable TE links
  Support for carrying the supported TS granularity
    i.e., 1.25G / 2.5G TS type
  Support any ODUs and ODUflex
    ODUflex has some features which are different from ODUj (j=0/1/2/2e/3/4)
  Support for differentiating between link multiplexing capacity and link rate capacity
    To support operator policies re transporting ODU connection services
  Support flexible priorities for resource reservation
    either no priorities or up to 8 priority levels as defined in [RFC4202]
  Support link bundling
    for the same or different types of ODU switching capable TE links
Need to be updated further

## Slide 6: ODU layer Hierarchy LSP
From data plane perspective, requirements of multi-stage multiplexing are being discussed in ITU-T SG15
  Introducing dedicated boards in a few specific places in the network to provide an ODUk tunnel to carry the client ODUj service
  Detection and representation of such constraints is FFS
The connection management/control model should be consistent with Hierarchy LSP about MLN (RFC4206, RFC4206bis, draft-ietf-ccamp-gmpls-mln-extensions and other related documents)
  One ODUj connection can be nested into another ODUk connection (j<k), which forms the LSP hierarchy in ODU layer
  How to create H-LSP is already defined in the existing documents
Termination cap. and switching cap. will be added in the routing

## Slide 7: Full-Lambda / Sub-Lambda LSP
Network policy/planning: provide pre-configured topology
Full-Lambda LSP:
  ODUk connection consuming the full lambda rate of OTUk links
  LO ODUj (j < k) can be multiplexed into full-lambda ODUk LSP
Sub-Lambda LSP:
  ODUj connection which can choose either directly over OTUk links or muxing into ODUk
A
B
C
D
E
ODU3 Full-Lambda LSP
OTU2
OTU2
OTU3
OTU3
ODU1 LSP
A
B
C
D
E
ODU2 Sub-Lambda LSP
OTU2
OTU2
OTU3
OTU3
service

## Slide 8: Next Steps
Refine the routing requirements
  Remove TS type
  Add termination cap. and switching cap.
  …(e.g., CCAMP requirements, )
Refine the description about full-lambda LSP and sub-lambda LSP
Refine it according to the feedback from the meeting or mailing list