## Slide 1: Information model for G.709 Optical Transport Network (OTN)
draft-bccg-ccamp-otn-g709-info-model-01
CCAMP WG, IETF 78th Maastricht

## Slide 2: Agenda
Target of the draft
Basic concept in the document
Next steps

## Slide 3: Target
[OTN-FRW] provides a list of requirements
This draft provides information needed from routing prospective to match with these requirements, analyzing how actual IETF constructs can help the implementation of these requirement and what is missing to improve LSA format efficiency.

## Slide 4: Basic concepts in the document (1)
Tributary Slot type : ITU-T defined two types of TS .
  This information is needed for bandwidth accounting and is not currently provided by the OSPF-TE.
LSA efficiency considerations
  [RFC4203] permits advertising single ISCD for signal type (e.g. min LSP Bw= max LSP BW for any ODU containers)
  This solution implies to advertise a huge number of ISCDs
  Efficiency can be improved compressing the advertisement (e.g. min LSP = ODU0 max LSP = ODU4 ) but losing information about what is actually supported in the hierarchy
    No implicit hierarchy like SDH/Sonet
    Presence of flexible containers: is ODUflex supported or not?
  Maximum LSP BW advertisement: is currently advertised in the common part of ISCD for every priority  only needed for ODUflex in OTN
  Unreserved BW : for TDM not useful to advertise BW with 32 bits to indicate floating point BW
    It is enough to have an integer representing number of Tributary Slots or number of containers
  A more optimized solution is required for providing the needed bandwidth accounting information, without proliferation of the number of ISCDs advertised

## Slide 5: Basic concepts in the document (2)
Bandwidth spatial allocation Unreserved resources advertisement per priority and per signal type
  Minimizes the number of crank-backs when restoring a high number of LSPs
  [RFC4203] permits advertising unreserved resource per priority but this is not enough to provide the exact spatial allocation in case of bundling.
    How many ODU3 service connections can be supported ? 1 or 2 ?
A
B
32 TS
24 TS
24 TS
Example: TE link bundling = 3-OTU3 – ODU2 (8TS), ODU3(32TS) signal type supported
16 TS allocated,
Max LSP BW = 32 TS – Unreserved BW = (32 + 24+ 24) = 80 TS
Number of ODU3 connection  80/32 = 2 this is not the reality of BW allocation

## Slide 6
ODU 3
ODU2
ODU2
ODU1
ODU1
ODU1
ODU1
ODU1
ODU1
ODU1
ODU1
ODU2
ODU1
ODU1
ODU1
ODU1
Unres bandwidth= 9 x 2.5Gbs= 22.5 Gbs
Is it possible to set up 2 ODU2(2x10Gbs)? NO
Example of single component link

## Slide 7: Basic concepts in the document (3)
Separate advertisement of bandwidth available at lambda granularity from the bandwidth available at sub-lambda granularity
  The ability to distinguish between link rate capacity and link multiplexing capacity is one of the requirements in [OTN-FWK].
  How a service (e.g., ODU connection service) is transported within an operator transport network is governed by operator policy. I.e., whether to support this connection service by:
    Dedicating an entire lambda capacity
    Leveraging sub-lambda multiplexing capability to transport the service
  [RFC4203] could achieve this distinction by advertising different ISCDs for (entire) lambda and sub-lambda, respectively
  A more optimized solution is required for providing this information, without proliferation of the number of ISCDs advertised

## Slide 8: Next steps
Collect comments/suggestions coming from the meeting
Refining the draft based on feedback and possible further requirement coming from G.709 and related work
New draft after the meeting

## Slide 9: QUESTIONS ?
THANK YOU