## Slide 1: OSPF-TE extensions for GMPLS Control of Evolving G.709 OTN
draft-ceccarelli-ccamp-gmpls-ospf-g709-02/03
CCAMP WG, IETF 78th Maastricht

## Slide 2: Agenda
Quick overview of version -02
Agreed requirements
Overview of version -03

## Slide 3: Encoding format - SubTLV
Priority flags
  Bit set = priority supported
  Non supported priorities are not advertised.
Tributary slot
  1,25 or 2,5 Gbps
Data Row
  Signal Type
    ODUk sublambda
    ODUk full lambda
    ODUflex, ODUflex resizable
  F bit (for ODUflex)
    F=1  Unres Bandwidth
    F=0  Max LSP Bandwidth
  Bandwidth @ Pi
    Unreserved bandwidth or Max LSP bandwidth expressed in number of TSs

## Slide 4: Example – t0
Supported priorities
  0,3,7
Tributary slot
  1,25 Gbps
Link component #1
  Full lambda: ODU2
  Sub lambda: ODU0, 1, Flex
Link component #2
  Full lambda: ODU3
  Sub lambda: ODU1, Flex
A
B
LC #1 – 8 TS
LC #2 – 32 TS

## Slide 5: Example – LSP setup
LSP1 – 35Gbps ODUFlex @P3 corresponding to 28 TS on LC#2
A
B
LC #1 – 8 TS
LC #2 – 32 TS

## Slide 6: Example – LSP preemption
LSP1 – 35Gbps ODUFlex @P3 corresponding to 28 TS on LC#2
LSP2 – 15 Gbps ODUFlex @P0 corresponding to 12 TS on LC#2
A
B
LC #1 – 8 TS
LC #2 – 32 TS

## Slide 7: Requirements – From OTN Framework
Multiple signal types
Multiple priorities
Scalability
Compact representation
ODUFlex
No precluding VCAT
Number of LSPs per signal type
Resource switched vs terminated, both
Consistent with CCAMP charter and work
  Reuse existing mechanisms wherever possible
  Extensions permitted, but need to be Generic wherever possible
Consensus

## Slide 8: New Solution (-03)
New sub-TLV
Signal types are scoped within Switching capability
Compress Signal Type and priority

## Slide 9: Example (-03)
Signal types
  ODU2 (1)
  ODU 3 (2)
Supported priorities
  1,2,5
M = 0
T = 1 (terminating capability)
S = 1 (switching capability)
A
B

## Slide 10: Compressing signal type and priority
Advertising once the bandwidth common to different:
  Signal Types
  Priorities
ODU2
ODU3
ODU2e
1
3
5
7

## Slide 11: Next steps
Collect feedbacks from the meeting
Publish version -03 with new solution
Collect feedback on the ML
Keep alignment with OTN Framework and G.709 Info Model.

## Slide 12: QUESTIONS ?
THANK YOU