## Slide 1: Requirement and Framework for Multi Stages Multiplexing Configuration in G.709 network
    draft-fuxh-ccamp-multi-stage-multiplex-config-req-01
    draft-fuxh-ccamp-multi-stage-multiplex-config-fwk-01
Xihua Fu, Malcolm Betts, ZTE Corporation
Ruiquan Jin, Xiaoli Huo, China Telecom
Han Li, China Mobile
Guangquan Wang, China Unicom
Guoying Zhang, Yunbin Xu, CATR

## Slide 2: Requirement for Multi Stages Multiplexing (MSM)
typical use case 1: interworking 1.25G TS/2.5G TS network
  Some legacy networks (2.5G TS) could only switch the ODU1/ODU2 without any visibility to ODU0/ODUflex.
  Multi stages multiplexing (MSM) facilitates the introduction of new ODU0 and ODUflex signals to an existing 2.5G TS network without having to upgrade every node in the 2.5G TS network.
10G Network
(1.25G TS)
two stages multiplexing for interworking between 1.25G TS and 2.5G TS network
40G Network
(2.5G TS)
10G Network
(1.25G TS)
X
X
0|2
2|0
X
1|0
0|2|3
3|2|0
0|2
X
0|2
2|0
OTU1
OTU2
ODU2 Tunnel
GE Service
Notes: ODU0/ODUflex can be mapped into ODU1/ODU2/ODU3 and transit across the 2.5G TS region.
ODU2/ODU3 effectively creates a tunnel through the ODU4 network that the ODU0, ODU1 and ODUflex can use.

## Slide 3: Requirement for Multi Stages Multiplexing (MSM)
typical use case 2: carrier’s carrier, regional-national core interconnection or network design based on tunnels.
  It is convenient to first multiplex ODU0 and ODUflex into ODU2 or ODU3 to minimize managed entities (e.g., cross connection) made in core network.
  A large number of circuits share the same endpoints (or even part of an overall path), it may be convenient to first multiplex those ODU0, ODU1 and ODUflex into ODU2 or ODU3 during network planning stage.
10G Network
(1.25G TS)
two stages multiplexing for multi-domain OTN application based on tunnel design network
100G Network
(1.25G TS)
40G Network
(1.25G TS)
X
X
0|2
2|0
X
2|0
0|3|4
4|3|0
0|3
X
0|3
3|0
OTU2
OTU3
ODU3 Tunnel
GE Service
Notes: ODU0/ODUflex can be mapped into ODU1/ODU2/ODU3 and transit across the 2.5G TS region.
ODU2/ODU3 effectively creates a tunnel through the ODU4 network that the ODU0, ODU1 and ODUflex can use.

## Slide 4: Requirement for Multi Stages Multiplexing Configuration
typical use case 1: interworking 1.25G TS/2.5G TS network
  Following GigE 1 and ODUflex 1 (e.g., 5*1.25G TS) share a ODU2 tunnel between G1 and G3. G1 and G3 have flexible MSM capability.
  Multi stages multiplexing hierarchy must be configured with ODU0-ODU2-ODU3 in G1 and G3 for GigE 1 service.
  Multi stages multiplexing hierarchy must be configured with ODUflex-ODU2-ODU3 in G1 and G3 for ODUflex 1 service.

## Slide 5: Requirement for Multi Stages Multiplexing Configuration
typical use case 2: carrier’s carrier, regional-national core interconnection or network design based on tunnels.
  Following GigE 2 and ODUflex 2 (e.g., 5*1.25G TS) share a ODU3 tunnel between G5 and G7. G5 and G7 have flexible MSM capability.
  Multi stages multiplexing/demultiplexing hierarchy must be configured with ODU0-ODU3-ODU4 in G5 and G7 for GigE 2 service.
  Multi stages multiplexing/demultiplexing hierarchy must be configured with ODUflex-ODU3-ODU4 in G5 and G7 for ODUflex 2 service.

## Slide 6: Framework for Multi Stages Multiplexing Configuration
New tunnels (FA-LSP) and fowarding adjacency have to be created because of multi stages multiplexing. These tunnels must be advertised in the routing topology as new TE links.
  Metric, SRLG, and protection attributes of these new TE links inherite from the parameters of the FA-LSPs.
  The bandwidth of these new tunnels (not filled by the initial request) should be shared for other later services as possible as it can.
  MSM capability is at a limited number of places in the network and the tunnels that are activated would be pre planned.
  The decision to advertise the MSM capability was taken based on the anticipated demand (policy) and creating the tunnel is just automating the final step of the planning/network configuration process.

## Slide 7: Framework for Multi Stages Multiplexing Configuration
Implementation of multi stages multiplexing:
  Integrated line card
  Cascade line card
Whatever the equipment implementation is, control plane should give a generic solution for the multi stages multiplexing configuration.

## Slide 8: Framework for Multi Stages Multiplexing Configuration
Control Plane:
  Routing
    It needs to advertise the MSM capability of nodes at a limited number of places in the network into the routing topology. ISCD and IACD are suggested to be reused and extended.
  Path Computation
    Path computation need to consider MSM capability constraint information and select a proper kind of MSM hierarchy of specific nodes along a E2E connection.
    PCE must consider the MSM hierarchies constraint request from PCC. PCEP protocol is suggested to be extended.
  Signaling
    Signaling message needs carry the MSM hierarchies for specific nodes that has been determined by path computation entity. RSVP-TE is suggested to be extended.
    MSM hierarchy for specific node must be configed to data plane after the node which needs to be support multi stages multiplexing receives the signaling of service creation.

## Slide 9: Next Steps
Refine the document according the feedback of meeting and mailing list